## Slide 1
SCULTRA
TECHNICAL DECISION REPORT
EDGE AI | MACHINE VISION | INDUSTRIAL QUALITY
Edge AI Machine Vision
for Industrial Quality Inspection
Technology, product architecture, supplier benchmarking and commercialisation strategy
Decision horizon | 2026-2032
Illustrative flagship report | August 2026
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
01
Notes: Cover visual is an original AI-generated asset created for SCULTRA.
[Sources]
- https://www.nist.gov/publications/2026-roadmap-artificial-intelligence-and-machine-learning-smart-manufacturing
- https://ifr.org/worldrobotics/report-2025
- https://ifr.org/ifr-press-releases/news/position-paper-on-ai-in-robotics
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 2
01 | EXECUTIVE SUMMARY
Build the modular edge node and constrain the beachhead
The opportunity is attractive when inspection failure is expensive, image presentation is controllable and model drift can be governed.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
02
RECOMMEND
Fund a 12-week pilot around assembly verification and controlled surface defects.
Buy cameras, optics, lighting and compute. Own the data workflow, model logic, validation method, line integration and fleet telemetry.
542k
Industrial robots installed in 2024
2
First-release use cases
7 mo
Illustrative base-case payback
EXECUTIVE CALL
Do not begin with custom camera hardware or a general-purpose vision platform. Prove the production decision and data loop first.
Source: IFR World Robotics 2025; NIST; SCULTRA analysis
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://ifr.org/worldrobotics/report-2025
- https://www.nist.gov/publications/2026-roadmap-artificial-intelligence-and-machine-learning-smart-manufacturing
- https://www.nist.gov/publications/detection-and-segmentation-manufacturing-defects-convolutional-neural-networks-and
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 3
01 | EXECUTIVE SUMMARY
Six decisions define the investment boundary
The recommended posture protects differentiation while limiting early hardware and integration risk.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
03
01
USE CASE
Assembly verification + controlled surface defects
02
PRODUCT
Modular edge inspection node
03
INFERENCE
Edge first; central training and fleet control
04
COMPUTE
Jetson Orin NX prototype; optimise after model stability
05
OWN
Data, models, validation, HMI, integration and telemetry
06
BUY
Camera, lens, lighting, compute, power and connectors
CONTROL POINT
The commercial control point is the production-ready intelligence layer, not the commodity image sensor or enclosure.
Source: SCULTRA recommendation informed by NIST manufacturing AI roadmap and supplier architectures
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nist.gov/publications/2026-roadmap-artificial-intelligence-and-machine-learning-smart-manufacturing
- https://www.siemens.com/en-gb/content/architecture-hub/ai-suite/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 4
01 | EXECUTIVE SUMMARY
The method links technical feasibility to a commercial decision
Public evidence was evaluated through five decision lenses; supplier claims are treated as inputs, not conclusions.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
04
1
Market need
Installed base, defect economics, workflow fit
2
Technology
Image formation, inference, MLOps, integration
3
Suppliers
Speed, control, lock-in, lifecycle and support
4
Product
Requirements, ownership boundary, cost and security
5
Commercial
Pilot gates, economics, roadmap and decision
Scoring model
Business value 30% | Deployability 25% | Product control 20% | Scale potential 15% | Risk 10%
SCOPE BOUNDARY
The report narrows the decision. It does not claim that one architecture fits every factory, part geometry or regulatory environment.
Source: SCULTRA methodology; public sources listed in slides 37-38
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nist.gov/publications/2026-roadmap-artificial-intelligence-and-machine-learning-smart-manufacturing
- https://ifr.org/worldrobotics/report-2025
- https://www.cognex.com/products/machine-vision/2d-machine-vision-systems/in-sight-d900
- https://www.keyence.com/products/vision/vision-sys/vs/specs/
- https://downloads-ctf.baslerweb.com/dg51pdwahxgw/1jFygRZWsQshfx9yU3lWuQ/bab86a82fb0254f4ac2486f7551af422/Computer_Vision_Portfolio_Brochure.pdf
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 5
02 | MARKET AND USE-CASE PRIORITY
A large automation base makes repeatable inspection scalable
Robot deployments indicate where automated lines and machine-vision adjacencies are already concentrated.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
05
542,000
Industrial robots installed in 2024
4.664m
Operational stock at year end
+9%
Operational stock growth
Deployment share by region
Asia 74%
Europe 16%
Americas 9%
Largest application sectors
0
10
20
30
Electronics
24%
Automotive
23%
Metal / machinery
16%
MARKET IMPLICATION
The first commercial focus should target automated electronics, automotive and precision-component lines where station replication is credible.
Source: International Federation of Robotics, World Robotics 2025
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://ifr.org/worldrobotics/report-2025
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 6
02 | MARKET AND USE-CASE PRIORITY
Inspection economics favour costly escapes and controlled presentation
AI creates value when it changes an operating decision, not merely when it detects an anomaly in a laboratory image.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
06
Low escape cost
High escape cost
Variable presentation
Repeatable presentation
Low priority
Engineering challenge
Automation hygiene
BEACHHEAD
High-cost escapes
Repeatable pose
Stable lighting
Economic test
Annual escape and rework cost is measurable
Inspection decision can change line action
Part pose, surface and illumination are controllable
False rejects have a known operating cost
COMMERCIAL GATE
Reject any pilot that cannot establish a credible line-level value baseline before model development begins.
Source: NIST manufacturing AI guidance and SCULTRA economic framing
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nist.gov/mep/rise-artificial-intelligence-ai-us-manufacturing-text-only
- https://www.nist.gov/publications/detection-and-segmentation-manufacturing-defects-convolutional-neural-networks-and
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 7
02 | MARKET AND USE-CASE PRIORITY
The use-case portfolio has a narrow, high-confidence beachhead
SCULTRA scored sixteen industrial vision applications on business value and deployability for a first product release.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
07
0
0
2
2
4
4
6
6
8
8
10
10
Assembly verification
Surface defects
Label / OCR
Packaging integrity
Weld inspection
PCB AOI
3D dimensional
BUSINESS VALUE
DEPLOYABILITY
Priority zone
Repeatable 2D presentation plus high-cost quality escapes
FIRST RELEASE
Assembly verification
Controlled surface defects
Adjacent: label/OCR and packaging integrity
PORTFOLIO CALL
Avoid welding, casting and 3D dimensional inspection in release one; value is high, but data and imaging complexity slow repeatable deployment.
Source: SCULTRA 1-10 scoring model informed by NIST and supplier application coverage
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nist.gov/publications/detection-and-segmentation-manufacturing-defects-convolutional-neural-networks-and
- https://www.cognex.com/products/machine-vision/2d-machine-vision-systems/in-sight-d900
- https://www.keyence.com/products/vision/vision-sys/vs/specs/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 8
02 | MARKET AND USE-CASE PRIORITY
Start with two use cases and design adjacencies deliberately
The beachhead shares image-capture, model, validation and integration primitives without forcing a universal vision product.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
08
Assembly verification
Presence, orientation, sequence, connector seating and component completeness under controlled pose.
Controlled surface defects
Scratches, dents, chips, contamination and finish anomalies with repeatable illumination and part presentation.
ADJACENT
Label / OCR
Packaging integrity
Seal inspection
Shared primitives
2D global shutter
Controlled lighting
Edge inference
PLC action
Audit trail
DEFER UNTIL THE PLATFORM IS PROVEN
Variable-pose welding | deep casting defects | multi-view 3D metrology | uncontrolled safety analytics
SCOPE GUARDRAIL
The use-case boundary is a product decision. Expanding it too early increases optics, data and validation variability faster than revenue.
Source: SCULTRA use-case prioritisation
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nist.gov/publications/detection-and-segmentation-manufacturing-defects-convolutional-neural-networks-and
- https://ifr.org/ifr-press-releases/news/position-paper-on-ai-in-robotics
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 9
03 | TECHNOLOGY AND PRODUCT ARCHITECTURE
The winning first product is an edge node, not a general vision platform
A modular node balances deployment speed with control of the data, model and production integration layers.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
09
Turnkey smart camera
DEPLOYMENT SPEED
Fastest
PRODUCT CONTROL
Low
LOCK-IN
High
Use as benchmark or simple-line alternative
Modular edge node
DEPLOYMENT SPEED
Medium
PRODUCT CONTROL
High
LOCK-IN
Low
DEFAULT PRODUCT ARCHITECTURE
Custom hardware
DEPLOYMENT SPEED
Slowest
PRODUCT CONTROL
Very high
LOCK-IN
Low
Optimise only after product-market fit
ARCHITECTURE CALL
The modular node preserves option value: it can adopt new sensors and accelerators without rebuilding the commercial intelligence layer.
Source: Supplier architectures and SCULTRA assessment
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.cognex.com/products/machine-vision/2d-machine-vision-systems/in-sight-d900
- https://www.keyence.com/products/vision/vision-sys/vs/specs/
- https://downloads-ctf.baslerweb.com/dg51pdwahxgw/1jFygRZWsQshfx9yU3lWuQ/bab86a82fb0254f4ac2486f7551af422/Computer_Vision_Portfolio_Brochure.pdf
- https://www.siemens.com/en-gb/content/architecture-hub/ai-suite/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 10
03 | TECHNOLOGY AND PRODUCT ARCHITECTURE
Classical vision and AI should be combined
Deterministic geometry handles known rules; learned models handle appearance variation and subtle defects.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
10
Classical vision
Fixture alignment
ROI localisation
Measurement
Presence and position
Hard tolerances
Learned vision
Classification
Object detection
Segmentation
Anomaly detection
Appearance tolerance
Decision fusion
Combine confidence, rule checks, process state and traceability into one auditable production decision.
Known geometry
Learned appearance
Fail-safe action
DESIGN RULE
A pure deep-learning stack increases validation burden. Use deterministic checks wherever the physics and tolerances are known.
Source: NIST defect-detection research; MVTec anomaly-detection methods
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nist.gov/publications/detection-and-segmentation-manufacturing-defects-convolutional-neural-networks-and
- https://www.mvtec.com/doc/halcon/2511/en/toc_deeplearning_anomalydetection.html
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 11
03 | TECHNOLOGY AND PRODUCT ARCHITECTURE
Edge-first inference should be the default
Keep the production decision local; use central infrastructure for training, registry, fleet control and audit.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
11
ON THE LINE
Capture
Camera + light
Infer
Model + rules
Act
PLC + reject
Record
Image + result
Target decision latency <=100 ms
CENTRAL CONTROL
Curated dataset and labelling
Training and model registry
Signed deployment packages
Fleet health and drift review
RESILIENCE RULE
Cloud dependency must never be in the reject-loop critical path. Loss of upstream connectivity should degrade monitoring, not inspection.
Source: Siemens Industrial Edge and AI Suite; LandingEdge
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.siemens.com/en-us/solutions/production-operations/industrial-edge-solutions/
- https://www.siemens.com/en-gb/content/architecture-hub/ai-suite/
- https://docs.landing.ai/landinglens-landingedge
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 12
03 | TECHNOLOGY AND PRODUCT ARCHITECTURE
The architecture must close the loop within one production cycle
The design is an operational control system with traceability, not a disconnected inference appliance.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
12
1
Trigger
Part + encoder
2
Acquire
Image + lighting
3
Decide
Model + rules
4
Act
PLC + reject
5
Record
Result + evidence
Illustrative latency budget
Trigger + exposure | 20 ms
Transfer + preprocess | 20 ms
Inference + rules | 40 ms
I/O + actuation | 20 ms
<=100 ms
MEASUREMENT RULE
Measure the entire trigger-to-action loop. Model latency alone is not a production performance metric.
Source: SCULTRA reference architecture informed by industrial-edge patterns
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.siemens.com/en-gb/content/architecture-hub/ai-suite/
- https://docs.landing.ai/landinglens-landingedge
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 13
03 | TECHNOLOGY AND PRODUCT ARCHITECTURE
Optimise compute for development risk before unit cost
Accelerator specifications are not directly comparable; software fit, model compatibility and lifecycle support matter more in the pilot.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
13
PLATFORM
AI THROUGHPUT
POWER
DEVELOPMENT FIT
SCULTRA POSTURE
NVIDIA Jetson Orin NX 16GB
Up to 157 sparse INT8 TOPS
10-40 W / MAXN SUPER
Highest
Prototype default
Hailo-8
26 TOPS
~2.5 W typical
Medium
Cost/power migration after model freeze
AMD Kria K26
1.4 TOPS
~7.5 W typical
Specialist
Consider where deterministic FPGA pipeline matters
NXP i.MX 95
2 TOPS NPU
Platform dependent
Embedded
Volume option for constrained models
COMPUTE CALL
Use Jetson Orin NX for the pilot to maximise iteration speed. Re-benchmark Hailo and embedded NPUs only after the model, preprocessing and latency envelope stabilise.
Source: Official module pages and product briefs; TOPS are vendor-reported and not apples-to-apples
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://developer.nvidia.com/embedded/jetson-modules
- https://hailo.ai/products/ai-accelerators/hailo-8-ai-accelerator/
- https://www.amd.com/content/dam/amd/en/documents/products/som/kria/k26/k26-product-brief.pdf
- https://www.nxp.com/products/i.MX95
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation] [Sources] - https://developer.nvidia.com/blog/?p=95089 - https://developer.nvidia.com/embedded/jetson-modules [/Sources]

## Slide 14
03 | TECHNOLOGY AND PRODUCT ARCHITECTURE
Global-shutter area-scan cameras cover the first product
A 5-12 MP monochrome or colour camera with C-mount optics is the lowest-risk foundation for the selected use cases.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
14
Area scan
2D parts, discrete triggers, broad lens choice
DEFAULT
Line scan
Continuous webs, cylindrical surfaces, high-resolution strips
LATER
3D vision
Height, volume and geometry that cannot be resolved in 2D
LATER
FIRST-PRODUCT CAMERA ENVELOPE
SENSOR
Global shutter
RESOLUTION
5-12 MP
INTERFACE
GigE or USB3 industrial
OPTICS
C-mount, lockable focus
PROTECTION
Industrial housing / IP as cell requires
IMAGE RULE
Do not specify resolution in isolation. Field of view, defect size, lens quality, exposure time and motion blur jointly determine usable pixels on defect.
Source: Basler portfolio; Cognex and KEYENCE device specifications
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://downloads-ctf.baslerweb.com/dg51pdwahxgw/1jFygRZWsQshfx9yU3lWuQ/bab86a82fb0254f4ac2486f7551af422/Computer_Vision_Portfolio_Brochure.pdf
- https://www.cognex.com/products/machine-vision/2d-machine-vision-systems/in-sight-d900/specifications
- https://www.keyence.com/products/vision/vision-sys/vs/specs/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 15
03 | TECHNOLOGY AND PRODUCT ARCHITECTURE
Lighting and fixturing determine more outcomes than model choice
Design the image-formation system first; the model can only learn the contrast and repeatability the optics provide.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
15
Bright field
Surface colour, print and broad contrast
Dark field
Scratches, edges and low-angle scatter
Backlight
Silhouette, dimension and presence
Diffuse dome
Curved or reflective surfaces
LOCK EXPOSURE, GAIN, WHITE BALANCE, PART POSE AND LIGHT OUTPUT IN THE VALIDATED RECIPE
ENGINEERING PRIORITY
Treat lighting, fixturing and optical recipes as version-controlled product assets. Uncontrolled image formation becomes model drift.
Source: SCULTRA engineering synthesis based on industrial camera and smart-camera specifications
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://downloads-ctf.baslerweb.com/dg51pdwahxgw/1jFygRZWsQshfx9yU3lWuQ/bab86a82fb0254f4ac2486f7551af422/Computer_Vision_Portfolio_Brochure.pdf
- https://www.cognex.com/products/machine-vision/2d-machine-vision-systems/in-sight-d900/specifications
- https://www.keyence.com/products/vision/vision-sys/vs/specs/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 16
03 | TECHNOLOGY AND PRODUCT ARCHITECTURE
Data quality is the durable competitive advantage
The moat is a governed loop that captures failure modes, improves coverage and preserves production context.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
16
Capture
Good, bad, borderline
Curate
Remove leakage and bias
Label
Defect taxonomy + severity
Train
Versioned data + model
Validate
Line metrics + drift
Learn
Mine escapes and false rejects
PRODUCTION CONTEXT
Part ID | lot | tool | recipe | operator | timestamp | image | decision
CONTINUOUS LEARNING LOOP
DATA RULE
Capture the context required to explain a decision later. Images without process metadata are a weak training asset and a weak audit trail.
Source: NIST smart-manufacturing AI roadmap; Siemens AI Suite data loop
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nist.gov/publications/2026-roadmap-artificial-intelligence-and-machine-learning-smart-manufacturing
- https://www.siemens.com/en-gb/content/architecture-hub/ai-suite/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 17
03 | TECHNOLOGY AND PRODUCT ARCHITECTURE
MLOps must be designed before fleet deployment
A scalable product needs controlled promotion, signed packages, rollback and evidence retention from the first pilot.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
17
DATASET
Immutable version
Coverage report
TRAIN
Reproducible run
Model card
VALIDATE
Offline + line gates
Failure modes
RELEASE
Signed package
Approval record
MONITOR
Drift + overrides
Fleet health
PROMOTION GATES
Recall | false rejects | latency | availability | repeatability | fail-safe behaviour
ROLLBACK
One-click return to the last approved model and recipe; no unlabeled model replacement on the line.
OPERATING MODEL
The pilot is the right moment to build release discipline. Retrofitting governance after ten stations creates avoidable technical debt.
Source: Siemens AI Suite; LandingLens and LandingEdge deployment documentation
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.siemens.com/en-gb/content/architecture-hub/ai-suite/
- https://docs.landing.ai/landinglens-landingedge
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 18
03 | TECHNOLOGY AND PRODUCT ARCHITECTURE
Acceptance metrics must separate detection from production performance
A model can look accurate offline and still fail the line through latency, false rejects, drift or poor recovery.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
18
>=99%
Priority-defect recall
Detection
<=2%
False reject rate
Operations
<=100 ms
Decision latency
System
>=99.5%
Station availability
Reliability
>=95%
Repeatability
Validation
PASS ONLY IF
Thresholds hold across shifts, lots, operators and planned lighting drift
Loss of camera, network or model service produces a safe and visible operating state
ASSUMPTION
These are proposed pilot gates, not external benchmarks. Final thresholds must be tied to defect criticality and line economics.
Source: SCULTRA recommended pilot acceptance framework
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nist.gov/publications/2026-roadmap-artificial-intelligence-and-machine-learning-smart-manufacturing
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 19
04 | SUPPLIER LANDSCAPE AND SOURCING
The supplier landscape separates into five control layers
No single vendor should own every layer of the first SCULTRA product architecture.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
19
Turnkey inspection
Cognex | KEYENCE
Fast deployment, integrated workflow
Industrial imaging
Basler | Allied Vision | FLIR
Sensors, cameras and interfaces
Edge compute
NVIDIA | Hailo | AMD | NXP
Inference and industrial compute
Vision software
MVTec | LandingAI | OpenVINO / TensorRT
Algorithms, training and runtime
Industrial edge
Siemens | PLC and gateway ecosystem
Fleet, integration and operations
SOURCING PRINCIPLE
Create supplier leverage by standardising interfaces and retaining a qualified alternate for each commodity layer.
Source: Official supplier product and architecture pages
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.cognex.com/products/machine-vision/2d-machine-vision-systems/in-sight-d900
- https://www.keyence.com/products/vision/vision-sys/vs/specs/
- https://downloads-ctf.baslerweb.com/dg51pdwahxgw/1jFygRZWsQshfx9yU3lWuQ/bab86a82fb0254f4ac2486f7551af422/Computer_Vision_Portfolio_Brochure.pdf
- https://developer.nvidia.com/embedded/jetson-modules
- https://hailo.ai/products/ai-accelerators/hailo-8-ai-accelerator/
- https://www.amd.com/content/dam/amd/en/documents/products/som/kria/k26/k26-product-brief.pdf
- https://www.nxp.com/products/i.MX95
- https://www.mvtec.com/doc/halcon/2511/en/toc_deeplearning_anomalydetection.html
- https://docs.landing.ai/landinglens-landingedge
- https://www.siemens.com/en-gb/content/architecture-hub/ai-suite/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 20
04 | SUPPLIER LANDSCAPE AND SOURCING
Turnkey smart cameras win on speed but constrain product control
They are credible deployment alternatives and useful benchmarks, but should not define the default SCULTRA product architecture.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
20
OPTION
STRENGTH
CONSTRAINT
BEST ROLE
Cognex In-Sight D900
Integrated deep / edge learning, IP67, up to 5 MP
Vendor workflow and hardware boundary
Benchmark; fast deployment where scope is stable
KEYENCE VS
Built-in AI, broad camera family, high supported frame rates
Closed ecosystem and commercial dependency
Simple high-speed applications and comparison
Modular edge node
Sensor choice, model control, telemetry and integration freedom
More engineering and validation responsibility
Default SCULTRA product architecture
COMPETITIVE TEST
Keep a turnkey camera in the pilot benchmark. If the modular node cannot outperform it on control, integration or economics, the product thesis needs revision.
Source: Cognex In-Sight D900 and KEYENCE VS official specifications
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.cognex.com/products/machine-vision/2d-machine-vision-systems/in-sight-d900
- https://www.cognex.com/products/machine-vision/2d-machine-vision-systems/in-sight-d900/specifications
- https://www.keyence.com/products/vision/vision-sys/vs/specs/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 21
04 | SUPPLIER LANDSCAPE AND SOURCING
Software platforms split between accessibility and engineering control
The recommended stack should simplify iteration without making the training interface the long-term product boundary.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
21
Accessibility
Engineering control
LandingLens / LandingEdge
Rapid labelling and deployment
MVTec HALCON
Industrial algorithm depth and anomaly detection
TensorRT / OpenVINO
Runtime optimisation and portable engineering control
Siemens AI Suite
Industrial-edge deployment and fleet integration
RECOMMENDED STACK
Open training code + industrial runtime + versioned data layer + product-owned HMI and validation
SOFTWARE CALL
Use low-code tools to accelerate discovery, but export the validated logic into a controlled product runtime before fleet scale.
Source: LandingAI, MVTec and Siemens official documentation
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://docs.landing.ai/landinglens-landingedge
- https://www.mvtec.com/doc/halcon/2511/en/toc_deeplearning_anomalydetection.html
- https://www.siemens.com/en-gb/content/architecture-hub/ai-suite/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 22
04 | SUPPLIER LANDSCAPE AND SOURCING
Component suppliers should be selected by layer
Qualification criteria should reflect failure modes and switching costs at each layer, not a single enterprise-vendor score.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
22
LAYER
PRIMARY CRITERIA
EXAMPLE OPTIONS
SOURCING POSTURE
Camera
Image quality, trigger, SDK, lifecycle
Basler; Allied Vision; FLIR
Dual-source by interface and sensor class
Optics
MTF, distortion, locking, availability
Kowa; Computar; Edmund
Approved lens list by field of view
Lighting
Uniformity, lifetime, controller API
CCS; Advanced Illumination; Smart Vision
Standard electrical and mechanical envelope
Compute
Runtime, thermals, lifecycle, security
NVIDIA; Hailo; AMD; NXP
Prototype for velocity; re-source at volume
Industrial I/O
Determinism, diagnostics, protocol
Siemens; Beckhoff; Phoenix Contact
Gateway abstraction; plant-specific variants
PROCUREMENT CALL
The interface specification is the sourcing asset. It makes supplier substitution an engineering change, not a product rewrite.
Source: Illustrative supplier set; Basler and compute-vendor official literature
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://downloads-ctf.baslerweb.com/dg51pdwahxgw/1jFygRZWsQshfx9yU3lWuQ/bab86a82fb0254f4ac2486f7551af422/Computer_Vision_Portfolio_Brochure.pdf
- https://developer.nvidia.com/embedded/jetson-modules
- https://hailo.ai/products/ai-accelerators/hailo-8-ai-accelerator/
- https://www.amd.com/content/dam/amd/en/documents/products/som/kria/k26/k26-product-brief.pdf
- https://www.nxp.com/products/i.MX95
- https://www.siemens.com/en-us/solutions/production-operations/industrial-edge-solutions/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 23
04 | SUPPLIER LANDSCAPE AND SOURCING
The best ecosystem is modular with qualified alternates
Standardise interfaces now so cost, supply and performance can be optimised without redesigning the intelligence layer.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
23
Camera
PRIMARY: GigE 5 MP
ALTERNATE: USB3 5 MP
Lighting
PRIMARY: strobed ring
ALTERNATE: bar / dome
Compute
PRIMARY: Orin NX
ALTERNATE: Hailo / embedded NPU
Line I/O
PRIMARY: digital + OPC UA
ALTERNATE: plant gateway
ECOSYSTEM RULE
Dual-source commodity layers, but single-source the product definition: data schema, model package, validation protocol and integration contract remain SCULTRA-owned.
Source: SCULTRA sourcing architecture informed by supplier interfaces
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://downloads-ctf.baslerweb.com/dg51pdwahxgw/1jFygRZWsQshfx9yU3lWuQ/bab86a82fb0254f4ac2486f7551af422/Computer_Vision_Portfolio_Brochure.pdf
- https://developer.nvidia.com/embedded/jetson-modules
- https://hailo.ai/products/ai-accelerators/hailo-8-ai-accelerator/
- https://www.siemens.com/en-us/solutions/production-operations/industrial-edge-solutions/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 24
05 | REFERENCE PRODUCT AND COMMERCIALISATION
Reference architecture: modular hardware, product-owned intelligence
The system isolates replaceable components from the SCULTRA data, model, validation and integration control plane.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
24
FACTORY CELL
Camera + optics
Global shutter
5-12 MP
C-mount
Lighting
Strobe control
Recipe ID
Health check
Edge node
Preprocess
Inference
Decision fusion
PLC / action
Trigger
Reject
Bypass
SCULTRA CONTROL PLANE
Data schema
Model package
Validation
HMI + audit
CENTRAL FLEET SERVICES
Dataset registry
Training + approval
Signed releases
Fleet telemetry
Drift and audit
REFERENCE DESIGN
The architecture permits local autonomy with central governance. Production continues safely when the upstream connection is unavailable.
Source: SCULTRA reference architecture; Siemens AI Suite and LandingEdge patterns
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.siemens.com/en-gb/content/architecture-hub/ai-suite/
- https://docs.landing.ai/landinglens-landingedge
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 25
05 | REFERENCE PRODUCT AND COMMERCIALISATION
Product concept: a rugged, modular edge inspection node
The enclosure is not the moat, but the physical design must support repeatable imaging, serviceability and safe factory integration.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
25
01
Replaceable camera and lens
02
Controlled, replaceable lighting
03
Rugged edge compute enclosure
04
M12 industrial power and I/O
05
Serviceable thermal path
PRODUCT RULE
Design for field replacement of the camera, lens, light and compute module. Avoid a sealed architecture that makes every upgrade a full-station replacement.
Source: SCULTRA concept; original AI-generated product visual
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis based on cited public sources and illustrative assumptions.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 26
05 | REFERENCE PRODUCT AND COMMERCIALISATION
The first product requirements should protect repeatability
Release one should be intentionally narrow and production-ready, with clear exclusions that prevent platform sprawl.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
26
MUST HAVE
5-12 MP global-shutter camera support
Recipe-controlled lighting and exposure
Hybrid classical + AI decision pipeline
Digital I/O plus OPC UA / gateway integration
Signed models, rollback and audit trail
Manual bypass and visible fail-safe state
WILL NOT HAVE IN RELEASE ONE
Custom image sensor or proprietary camera interface
Multi-view 3D metrology
Cloud dependency in the reject loop
Universal no-code application builder
Autonomous model promotion without approval
Unbounded use-case and defect taxonomy
PRD PRINCIPLE
A narrow product can still be architecturally extensible. Release discipline is the mechanism that preserves speed and validation quality.
Source: SCULTRA product requirements synthesis
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nist.gov/publications/2026-roadmap-artificial-intelligence-and-machine-learning-smart-manufacturing
- https://digital-strategy.ec.europa.eu/en/policies/cra-summary
- https://webstore.iec.ch/en/publication/34421
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 27
05 | REFERENCE PRODUCT AND COMMERCIALISATION
Build the intelligence layer and buy the commodity layers
Ownership should follow differentiation, switching cost and the evidence required to defend a production decision.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
27
BUY AND QUALIFY
Camera + sensor
Mature supply and interfaces
Optics
Application-specific but not differentiating
Lighting hardware
Qualify uniformity and controller
Compute module
Prototype velocity, later cost optimisation
Power + connectors
Industrial compliance and availability
BUILD AND OWN
Data workflow
Coverage, traceability and learning loop
Model + rules
Decision logic and confidence policy
Validation method
Defensible line acceptance
HMI + integration
Operator trust and production fit
Fleet telemetry
Lifecycle control and recurring value
OWNERSHIP CALL
Do not outsource the validation protocol. It is the bridge between model performance, customer acceptance and product liability.
Source: SCULTRA build-versus-buy recommendation
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nist.gov/publications/2026-roadmap-artificial-intelligence-and-machine-learning-smart-manufacturing
- https://www.siemens.com/en-gb/content/architecture-hub/ai-suite/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 28
05 | REFERENCE PRODUCT AND COMMERCIALISATION
Hardware cost should stay below integration and validation cost
The pilot must buy learning, not over-engineered hardware. Unit-cost optimisation follows a stable model and repeatable deployment recipe.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
28
Illustrative pilot cost structure
Hardware
$18k
Integration
$22k
Data + model
$12k
Validation
$8k
Buffer
$5k
$65k illustrative station pilot
$4k-$8k
Target hardware BOM per station after pilot
Cost-down sequence
1
Freeze model and imaging recipe
2
Measure compute and thermal headroom
3
Qualify lower-cost accelerator
4
Optimise enclosure at volume
COST CAVEAT
Illustrative costs are planning assumptions. Replace them with quotations and customer-specific integration effort before investment approval.
Source: SCULTRA illustrative cost model; not supplier quotations
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis based on cited public sources and illustrative assumptions.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 29
05 | REFERENCE PRODUCT AND COMMERCIALISATION
Cybersecurity must be a product requirement
Industrial AI nodes are networked products with software lifecycle obligations, not isolated cameras.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
29
Secure boot
Verified firmware and trusted root
Signed updates
Approved model and software packages
SBOM
Component and dependency inventory
Access control
Least privilege and service accounts
Vulnerability process
Monitor, assess, patch and disclose
Network segmentation
No direct internet dependency in the cell
EU CYBER RESILIENCE ACT
Reporting obligations: 11 Sep 2026 | Main product obligations: 11 Dec 2027
SECURITY CALL
Create the SBOM, update mechanism and vulnerability process during the pilot. They are architecture choices, not documentation tasks.
Source: European Commission CRA summary and reporting guidance; IEC 62443-4-2
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://digital-strategy.ec.europa.eu/en/policies/cra-summary
- https://digital-strategy.ec.europa.eu/en/policies/cra-reporting
- https://webstore.iec.ch/en/publication/34421
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 30
05 | REFERENCE PRODUCT AND COMMERCIALISATION
Validation must test drift, failure recovery and operator behaviour
A production system is validated across time and operating states, not only against a held-out image set.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
30
IMAGE ROBUSTNESS
Lighting drift
Focus shift
Pose tolerance
Surface variation
MODEL PERFORMANCE
Critical recall
False rejects
Borderline parts
Novel defects
SYSTEM RECOVERY
Camera loss
Network loss
Thermal limit
Rollback
HUMAN OPERATION
Override reason
Bypass control
Alarm clarity
Maintenance
VALIDATION EVIDENCE
Approved dataset | test protocol | failure log | operator sign-off | rollback proof | acceptance record
VALIDATION GATE
No release is production-ready until the safe state, bypass and rollback behaviour have been demonstrated under fault injection.
Source: SCULTRA validation framework informed by NIST, EU machinery regulation and IEC 62443
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nist.gov/publications/2026-roadmap-artificial-intelligence-and-machine-learning-smart-manufacturing
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=celex%3A32023R1230
- https://webstore.iec.ch/en/publication/34421
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 31
06 | PILOT, ECONOMICS AND ROADMAP
A 12-week pilot can prove the architecture and economics
The plan front-loads image formation and value baselining, then gates model, integration and operating readiness.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
31
WEEK 1-2
Baseline
Defect taxonomy
Economics
Image study
WEEK 3-4
Image system
Fixture
Lighting
Camera recipe
WEEK 5-7
Model
Dataset
Hybrid pipeline
Offline gates
WEEK 8-9
Integrate
PLC
HMI
Traceability
WEEK 10-11
Run
Shift trials
Drift
Recovery
WEEK 12
Decide
Acceptance
ROI
Scale plan
GO / NO-GO GATES
Week 2 value baseline | Week 4 image repeatability | Week 7 offline performance | Week 11 line stability | Week 12 investment decision
PILOT DISCIPLINE
Stop early if image formation is unstable or the value baseline is weak. A failed early gate is cheaper than a polished demonstration with no production case.
Source: SCULTRA proposed pilot plan
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis based on cited public sources and illustrative assumptions.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 32
06 | PILOT, ECONOMICS AND ROADMAP
Illustrative economics support a pilot, not a fleet commitment
Base-case payback is attractive if annual gross benefit reaches $125k and operating cost remains controlled.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
32
Annual gross benefit ($k)
Conservative
$75k
Base
$125k
Upside
$190k
Payback on $65k capex
13 mo
Conservative
7.1 mo
Base
4.5 mo
Upside
ASSUMPTIONS
$65k system capex | $15k annual operating cost | benefits combine avoided escapes, reduced manual inspection and recovered throughput
ECONOMIC CAVEAT
Approve the pilot against a customer-specific value baseline. Do not publish these scenarios as market pricing or guaranteed savings.
Source: SCULTRA illustrative scenario model; replace with site-level data
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis based on cited public sources and illustrative assumptions.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 33
06 | PILOT, ECONOMICS AND ROADMAP
An 18-month roadmap should sequence evidence before scale
The product earns broader scope only after repeatable deployment and a governed learning loop are proven.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
33
1
MONTH 0-3
Prove
Pilot cell
Image recipe
Acceptance metrics
2
MONTH 4-6
Productise
Rugged enclosure
Installer workflow
Security baseline
3
MONTH 7-9
Replicate
Second line
Supplier alternates
Fleet telemetry
4
MONTH 10-12
Commercialise
Offer design
Partner model
Support process
5
MONTH 13-18
Expand
Adjacent use cases
Cost-down
Regional compliance
EXPANSION GATES
Repeatable installation | accepted fleet telemetry | qualified alternate compute | supportable gross margin | regulatory readiness
SCALE GATE
Do not launch the adjacent use-case portfolio until the second-line deployment demonstrates that the product, not the founding engineering team, carries the know-how.
Source: SCULTRA product roadmap
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://digital-strategy.ec.europa.eu/en/policies/cra-summary
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=celex%3A32023R1230
- https://digital-strategy.ec.europa.eu/en/faqs/navigating-ai-act
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 34
07 | FINAL RECOMMENDATION
Approve the pilot with a modular architecture and hard gates
The opportunity is sufficiently attractive to test, but the product thesis must be proven through production evidence.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
34
APPROVE
Fund a 12-week edge-inspection pilot.
Constrain scope to assembly verification and controlled surface defects. Prototype on Jetson Orin NX, retain a turnkey-camera benchmark, and own the data, validation and integration layers.
FUND
One station and two defect families
Imaging, model and PLC integration
Security and MLOps baseline
DO NOT FUND YET
Custom camera or enclosure tooling
3D, weld or casting expansion
FINAL CALL
The next commitment is a disciplined experiment, not a platform build. Scale follows evidence.
Source: SCULTRA final recommendation based on preceding evidence
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://ifr.org/worldrobotics/report-2025
- https://www.nist.gov/publications/2026-roadmap-artificial-intelligence-and-machine-learning-smart-manufacturing
- https://www.cognex.com/products/machine-vision/2d-machine-vision-systems/in-sight-d900
- https://www.keyence.com/products/vision/vision-sys/vs/specs/
- https://downloads-ctf.baslerweb.com/dg51pdwahxgw/1jFygRZWsQshfx9yU3lWuQ/bab86a82fb0254f4ac2486f7551af422/Computer_Vision_Portfolio_Brochure.pdf
- https://developer.nvidia.com/embedded/jetson-modules
- https://digital-strategy.ec.europa.eu/en/policies/cra-summary
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 35
07 | FINAL RECOMMENDATION
Six questions must be answered before scale investment
These decision gates convert the pilot from a demonstration into a defensible product and sourcing decision.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
35
01
VALUE
What is the annual cost of escapes, false rejects and manual inspection on the target line?
02
IMAGE
Can part pose, lighting and surface presentation be controlled across shifts and lots?
03
MODEL
Do critical recall and false-reject gates hold on unseen production data?
04
SYSTEM
Does the full trigger-to-action loop meet latency, availability and recovery requirements?
05
PRODUCT
Can a second line be installed without bespoke model and integration work?
06
COMMERCIAL
Do support effort, BOM and customer value support an attractive margin and payback?
DECISION STANDARD
A yes on model performance is insufficient. Scale requires simultaneous proof of value, image repeatability, system reliability, replicability and commercial supportability.
Source: SCULTRA decision gates
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis based on cited public sources and illustrative assumptions.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 36
08 | METHOD, CAVEATS AND SOURCES
Assumptions and scoring method
The conclusions are directionally robust, but economics, vendor selection and compliance scope require project-specific validation.
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
36
USE-CASE SCORING
Business value
30%
Deployability
25%
Product control
20%
Scale potential
15%
Risk adjustment
10%
KEY ASSUMPTIONS
Controlled 2D presentation is feasible
$65k pilot capex is illustrative
Benefit scenarios are not customer quotes
Vendor claims require application testing
CAVEATS
TOPS are not directly comparable across vendors. Regulations depend on intended use and market. Prices, product specifications and availability can change. The use-case scores are SCULTRA judgements, not measured market benchmarks.
PUBLICATION CHECK
Before external publication, revalidate all time-sensitive vendor specifications, regulatory dates and commercial assumptions.
Source: SCULTRA methodology and caveats
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://digital-strategy.ec.europa.eu/en/policies/cra-summary
- https://digital-strategy.ec.europa.eu/en/faqs/navigating-ai-act
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=celex%3A32023R1230
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 37
DECISION REQUIRED
Approve a 12-week pilot
with explicit production gates
Scope
Assembly verification + controlled surface defects
Architecture
Modular edge node; SCULTRA-owned intelligence layer
Funding
$65k illustrative pilot envelope
APPROVE IF
A target line and owner are named
Value baseline can be measured
Pilot gates are contractually explicit
NEXT: site selection + defect workshop
SCULTRA SERVICES
EDGE AI MACHINE VISION | 2026-2032
39
Notes: SCULTRA decision page. All economics are illustrative until replaced with site-level evidence.
[Sources]
- SCULTRA analysis based on cited public sources and illustrative assumptions.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]