## Slide 1
ILLUSTRATIVE FLAGSHIP REPORT
EU Digital Product Passport
& Product Traceability
Regulatory Readiness, Technology Architecture, Vendor Landscape and Implementation Strategy | 2026 to 2030
Illustrative report | August 2026
Regulation | Architecture | Vendor assessment | Implementation
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
01
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 2
EXECUTIVE SUMMARY
Build a product-data operating system, not a QR-code project
Five findings connect the regulatory mandate to architecture, data ownership, vendor choice and implementation.
Sources:
EU regulations | European Commission | SCULTRA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
02
01
Mandate
The EU Registry is operational and specified batteries require passports from 18 February 2027.
02
Data
The visible label is simple; evidence lineage, supplier data and lifecycle change control are not.
03
Architecture
A federated control plane can reuse authoritative ERP, PLM, PIM, LCA, QMS and service data.
04
Vendors
No platform leads every system-of-record, traceability, identity, interoperability and sector dimension.
05
Action
Use a 90-day architecture proof, then close one regulated cohort before scaling the portfolio.
Decision: govern one reusable product-data capability, then configure product-specific passport rules and experiences.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://eur-lex.europa.eu/eli/reg/2023/1542/oj
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport_en
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. The EUR 3.21m three-year TCO is a SCULTRA scenario: EUR 1.38m one-time plus EUR 0.61m annual run cost for three years. [/QC2 Validation] [Sources] - https://eur-lex.europa.eu/eli/reg/2024/1781/eng - https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX%3A32023R1542 - https://single-market-economy.ec.europa.eu/news/digital-product-passport-registry-now-live-2026-07-20_en - https://single-market-economy.ec.europa.eu/single-market/goods/european-standards/harmonised-standards/digital-product-passport-dpp_en [/Sources]

## Slide 3
EXECUTIVE NUMBERS
The first compliance wave is live, while enterprise readiness remains a data problem
The Registry is operational; six standards are published; specified batteries require passports from 18 February 2027.
Sources:
European Commission | EU law | SCULTRA model
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
03
REGULATORY
LIVE
EU DPP Registry
Operational since 20 July 2026
TECHNICAL
6
harmonised standards
Published for protocols, IDs, carriers, storage, APIs and interoperability
DEADLINE
18 FEB 2027
first mandatory wave
Specified LMT, industrial >2 kWh and EV batteries
MODEL
58 / 100
illustrative readiness
Supplier evidence, governance and access controls need remediation
Model context
120,000 candidate records | EUR 1.38m one-time implementation | EUR 0.61m annual run cost | EUR 3.21m three-year TCO
All portfolio and cost values are editable SCULTRA assumptions.
The regulatory facts are current; the enterprise numbers are a transparent planning scenario, not a benchmark.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://single-market-economy.ec.europa.eu/news/digital-product-passport-registry-now-live-2026-07-20_en
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
- https://eur-lex.europa.eu/eli/reg/2023/1542/oj
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 4
REPORT GUIDE
Contents
A decision path from regulatory scope to architecture, vendors and a stage-gated implementation.
Sources:
SCULTRA analysis
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
04
01
Regulatory Mandate & Business Context
Scope, timing, audiences, readiness and economics
Slides 5 to 17
02
Technology & Data Architecture
Identity, source systems, Registry, access and releases
Slides 18 to 28
03
Vendor & Delivery Ecosystem
Archetypes, longlist, scorecard, sourcing and risk
Slides 29 to 39
04
Implementation Strategy
Starting wedge, design principles and 90-day sprint
Slides 40 to 44
The storyline moves from legal obligation to execution design, then tests vendor fit and implementation readiness.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 5
01
Regulatory Mandate & Business Context
What DPP is, who must act, when product groups enter scope and where the implementation burden sits.
SCULTRA REPORT SERIES
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
05
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 6
MARKET DEFINITION
A DPP is a governed product record with a physical access point
The passport connects a persistent identifier to structured, role-based and lifecycle-aware product data.
Sources:
Regulation (EU) 2024/1781 | European Commission
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
06
1
PHYSICAL PRODUCT
Product, packaging or documentation carries the access point
2
IDENTITY + CARRIER
Persistent unique identifier via QR, Data Matrix, NFC or equivalent
3
PASSPORT RECORD
Structured, machine-readable data with evidence and lifecycle status
4
ROLE-BASED SERVICES
Consumers, partners, repairers, recyclers, authorities and customs
What it is
A product-specific dataset
A persistent identity relationship
An interoperable access mechanism
A controlled lifecycle record
What it is not
A static web page, a marketing QR code, a universal data schema or a replacement for ERP, PLM and PIM.
The carrier opens the door; compliance depends on the governed record and the operating controls behind it.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport_en
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. The EUR 3.21m three-year TCO is a SCULTRA scenario: EUR 1.38m one-time plus EUR 0.61m annual run cost for three years. [/QC2 Validation] [Sources] - https://eur-lex.europa.eu/eli/reg/2024/1781/eng - https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX%3A32023R1542 - https://single-market-economy.ec.europa.eu/news/digital-product-passport-registry-now-live-2026-07-20_en - https://single-market-economy.ec.europa.eu/single-market/goods/european-standards/harmonised-standards/digital-product-passport-dpp_en [/Sources]

## Slide 7
WHY NOW
The system has moved from policy design to operational execution
The EU Registry went live in July 2026, with the first mandatory product wave less than seven months later.
Sources:
European Commission | EUR-Lex
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
07
JUL 2024
Framework in force
ESPR establishes the DPP system and essential requirements.
APR 2025
Portfolio priorities
Working Plan names product groups through 2030.
20 JUL 2026
Registry operational
Economic operators can test registration and technical guidance.
18 FEB 2027
First hard deadline
Specified batteries placed on the EU market need a passport.
Execution window
The first regulated cohort is under seven months away as of 8 August 2026.
Architecture, data ownership and supplier remediation cannot be compressed into label production.
The right response is a controlled pilot now, not a wait-and-see technology procurement.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://single-market-economy.ec.europa.eu/news/digital-product-passport-registry-now-live-2026-07-20_en
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport_en
- https://eur-lex.europa.eu/eli/reg/2023/1542/oj
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. The EUR 3.21m three-year TCO is a SCULTRA scenario: EUR 1.38m one-time plus EUR 0.61m annual run cost for three years. [/QC2 Validation] [Sources] - https://eur-lex.europa.eu/eli/reg/2024/1781/eng - https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX%3A32023R1542 - https://single-market-economy.ec.europa.eu/news/digital-product-passport-registry-now-live-2026-07-20_en - https://single-market-economy.ec.europa.eu/single-market/goods/european-standards/harmonised-standards/digital-product-passport-dpp_en [/Sources]

## Slide 8
REGULATORY STACK
The obligation is assembled across framework, product and technical rules
ESPR sets the system; product acts define content and granularity; standards define interoperable execution.
Sources:
EU law | European Commission
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
08
1
FRAMEWORK
ESPR Regulation (EU) 2024/1781
Defines DPP principles, Registry, open standards, access and no lock-in
2
PRODUCT RULES
Delegated acts and standalone EU legislation
Define content, granularity, carrier placement, access and transition
3
TECHNICAL STANDARDS
EN 18216, 18219, 18220, 18221, 18222, 18223
Define protocols, identity, carriers, persistence, APIs and interoperability
4
ENTERPRISE CONTROLS
Policies, data contracts, evidence, security and operations
Convert requirements into a repeatable product-data release process
Do not hard-code product content into the platform core; keep product-rule semantics configurable.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://eur-lex.europa.eu/eli/reg/2023/1542/oj
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
- https://green-forum.ec.europa.eu/news/2025-2030-working-plan-2025-07-11_en
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. The EUR 3.21m three-year TCO is a SCULTRA scenario: EUR 1.38m one-time plus EUR 0.61m annual run cost for three years. [/QC2 Validation] [Sources] - https://eur-lex.europa.eu/eli/reg/2024/1781/eng - https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX%3A32023R1542 - https://single-market-economy.ec.europa.eu/news/digital-product-passport-registry-now-live-2026-07-20_en - https://single-market-economy.ec.europa.eu/single-market/goods/european-standards/harmonised-standards/digital-product-passport-dpp_en [/Sources]

## Slide 9
IMPLEMENTATION TIMELINE
Regulatory waves create a portfolio sequencing problem through 2030
Batteries lead in 2027; iron and steel, textiles, aluminium, tyres, construction, furniture and other groups follow.
Sources:
European Commission indicative DPP timeline
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
09
2026
Registry live
Six standards
Iron and steel act indicated
2027
Battery passports
Construction and service-provider rules
Textiles, aluminium and tyres acts indicated
2028
Furniture act indicated
Construction implementation expands
Mid-term policy review
2029
Mattresses
ICT products
Recycled-content measures
2030
Working-plan horizon
Portfolio-scale operating model
Further product acts
The dates are an indicative Commission roadmap; each product obligation follows its applicable act and transition period.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport_en
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport/economic-operators_en
- https://green-forum.ec.europa.eu/news/2025-2030-working-plan-2025-07-11_en
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. The EUR 3.21m three-year TCO is a SCULTRA scenario: EUR 1.38m one-time plus EUR 0.61m annual run cost for three years. [/QC2 Validation] [Sources] - https://eur-lex.europa.eu/eli/reg/2024/1781/eng - https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX%3A32023R1542 - https://single-market-economy.ec.europa.eu/news/digital-product-passport-registry-now-live-2026-07-20_en - https://single-market-economy.ec.europa.eu/single-market/goods/european-standards/harmonised-standards/digital-product-passport-dpp_en [/Sources]

## Slide 10
ACCESS RIGHTS
One passport serves different audiences through differentiated access
Consumers, commercial partners, repairers, recyclers, authorities and customs should not see the same information.
Sources:
Regulation (EU) 2024/1781 | Battery Regulation
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
10
Audience
Identity and basic data
Sustainability and circularity
Commercial or confidential
Authority evidence
Consumer
Public
Public
No
No
Business partner
Public
Agreed subset
Permissioned
No
Repairer or recycler
Public
Functional subset
Legitimate-interest subset
No
Market authority
Full
Full
As required
Full
Customs
Identifier and commodity data
Limited
No
Verification access
PUBLIC
PERMISSIONED
AUTHORITY
Access is defined by product rules and purpose, not by one universal audience model.
Design access as a policy layer so product rules can change without rebuilding the passport data store.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://eur-lex.europa.eu/eli/reg/2023/1542/oj
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 11
MATURITY MODEL
Compliance maturity progresses from a static page to a governed data product
The target state is automated publication, evidence lineage, controlled access and lifecycle updates.
Sources:
CIRPASS-2 | SCULTRA maturity model
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
11
1
STATIC
Web page
Manual content, weak lineage
2
LINKED
Product ID
Structured fields, basic ownership
3
CONTROLLED
DPP pilot
Evidence, roles, persistence
4
AUTOMATED
Release engine
Source integrations and change events
5
VALUE-ENABLED
Data product
Circularity, service and ecosystem use
Target level 3 for the first regulatory pilot, then industrialise levels 4 and 5 across the portfolio.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://cirpass2.eu/project-results/
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 12
VALUE CASE
DPP can convert a compliance burden into a reusable product-data capability
The same trusted record can support market access, service, repair, resale, circularity and claims assurance.
Sources:
European Commission | CIRPASS-2 | SCULTRA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
12
01
MARKET ACCESS
Demonstrate required product information and support surveillance.
02
CLAIMS ASSURANCE
Link sustainability and sourcing claims to current evidence.
03
SERVICE + REPAIR
Expose parts, maintenance and repair information to authorised actors.
04
RESALE + AUTHENTICITY
Maintain product identity and lifecycle history across ownership changes.
05
CIRCULARITY
Give refurbishers and recyclers data needed for higher-value recovery.
06
DATA REUSE
Publish one governed fact set into multiple regulatory and commercial workflows.
Prioritise compliance and data reuse first; consumer engagement is valuable only when the underlying record is trusted.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport_en
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport/economic-operators_en
- https://cirpass2.eu/project-results/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 13
READINESS GAP
The illustrative enterprise starts at 58 out of 100 readiness
Supplier data, evidence lineage, governance and access controls lag internal master-data completeness.
Sources:
SCULTRA editable readiness model
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
13
Product identity
68
Internal product data
78
Supplier data
52
Evidence lineage
55
Integration automation
50
Governance and controls
45
Access, privacy and security
40
WEIGHTED SCORE
58
out of 100
Priority remediation
Audience-tier controls
Product-data release authority
Supplier evidence contract
Six source-system interfaces
The program can pilot, but it should not scale until access, governance and supplier evidence cross the agreed gate.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 14
IMPLEMENTATION CONSTRAINTS
The hardest dependencies sit outside the DPP application
Identity quality, product granularity, supplier evidence, system ownership and change control determine whether passports remain true.
Sources:
EU law | CIRPASS-2 | SCULTRA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
14
PASSPORT TRUTH
The published record must remain aligned to the physical product.
Identity drift
Model, batch and item relationships are unclear.
Supplier evidence
Primary data, proof and rights are incomplete.
System ownership
No authoritative source is assigned per field.
Lifecycle change
Engineering, repair and service events do not propagate.
Access conflict
Trade secrets, privacy and legitimate interest differ.
Persistence
Data must remain accessible after vendor or company exit.
The implementation bottleneck is cross-functional data control, not the front-end experience.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://cirpass2.eu/project-results/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 15
ECONOMICS
A 120,000-record program implies a three-year TCO of about EUR 3.2 million
The illustrative cost is driven by integration, data remediation, supplier onboarding and the recurring control function.
Sources:
SCULTRA editable implementation model
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
15
One-time implementation | EUR 1.38m
Integrations
EUR 450k
Platform setup
EUR 180k
Data remediation
EUR 180k
Testing + change
EUR 160k
Supplier onboarding
EUR 150k
Architecture
EUR 140k
Readiness
EUR 120k
THREE-YEAR TCO
EUR 3.21m
EUR 1.38m one-time + EUR 0.61m annual run cost
Annual operating model | EUR 0.61m
EUR 220k
Platform
EUR 180k
Governance
EUR 120k
Support
EUR 90k
Supplier ops
EUR 5.08 annual run cost per candidate record at full scale
Illustrative costs expose the main drivers; replace them with source-system complexity, supplier tiers and vendor proposals.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. The EUR 3.21m three-year TCO is a SCULTRA scenario: EUR 1.38m one-time plus EUR 0.61m annual run cost for three years. [/QC2 Validation] [Sources] - https://eur-lex.europa.eu/eli/reg/2024/1781/eng - https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX%3A32023R1542 - https://single-market-economy.ec.europa.eu/news/digital-product-passport-registry-now-live-2026-07-20_en - https://single-market-economy.ec.europa.eu/single-market/goods/european-standards/harmonised-standards/digital-product-passport-dpp_en [/Sources]

## Slide 16
READINESS GATES
Seven evidence gates separate a prototype from a compliant operating capability
The program should not scale until legal scope, identity, data, access, persistence, controls and operations are proven.
Sources:
EU law | standards | SCULTRA framework
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
16
01
LEGAL SCOPE
Applicable products, roles, timing and accountable economic operator
02
IDENTITY
Persistent identifier, granularity, carrier and resolver
03
DATA
Authoritative sources, owners, semantics, quality and validity
04
ACCESS
Audience tiers, purpose, privacy, trade secrets and logging
05
PERSISTENCE
Storage, backup, uptime, archive and provider exit
06
CONFORMITY
Evidence, approvals, registration and audit trail
07
OPERATIONS
Change events, incident response, monitoring and release control
Make every gate evidence-based and binary enough to stop scale when the operating capability is not ready.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
- https://eur-lex.europa.eu/legal-content/EN/ALL/?uri=intcom:Ares(2024)8031852
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 17
SECTION SYNTHESIS
The obligation arrives by product group, but the foundation is enterprise-wide
Build one reusable control plane and publish product-specific passports through configurable rules.
Sources:
European Commission | SCULTRA synthesis
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
17
CHAPTER 01 CONCLUSION
Product rules arrive in waves. The foundation should not.
One reusable identity, evidence, access and release-control plane can publish configurable passports across product groups.
01
Do now
Map portfolio scope, identity, source systems, suppliers and evidence.
02
Do once
Build the canonical model, access engine, audit trail and persistence controls.
03
Configure later
Apply product-specific fields, granularity, audiences and experiences as acts mature.
Operating principle: centralise control, federate authoritative data and configure regulatory variation.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport_en
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport/economic-operators_en
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 18
02
Technology & Data Architecture
How identity, source systems, orchestration, access control, the EU Registry and user experiences fit together.
SCULTRA REPORT SERIES
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
18
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 19
ARCHITECTURE METHOD
Separate systems of record, passport orchestration and access experiences
The architecture should keep authoritative data at source while creating a durable, auditable publication layer.
Sources:
CIRPASS-2 | EN 18216 to EN 18223
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
19
SYSTEMS OF RECORD
ERP | PLM | PIM | LCA | QMS | MES | service
Own product facts and evidence
DPP CONTROL PLANE
Canonical model | rules | evidence | access | audit
Assemble, validate, publish and monitor
ACCESS EXPERIENCES
Registry | resolver | APIs | consumer | partner | authority
Deliver the right view to the right actor
Authoritative at source
Open interfaces
Configurable semantics
Portable identity
Evidence by design
Observable operations
The DPP layer is a publication and control plane, not a second master-data system.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://cirpass2.eu/project-results/
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 20
REFERENCE ARCHITECTURE
A federated control plane is the lowest-regret enterprise pattern
The DPP platform assembles trusted data, applies rules and access, registers identifiers and serves multiple audiences.
Sources:
CIRPASS-2 | EU Registry | SCULTRA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
20
ERP
PLM
PIM
LCA
QMS
MES
SERVICE
INGEST + QUALITY
APIs, files, events
Schema mapping
Completeness and proof checks
DPP CONTROL PLANE
Canonical product graph
Product-rule configuration
Evidence and validity
Audience policy engine
Lifecycle release workflow
Audit and monitoring
IDENTITY + RESOLUTION
Persistent ID
Carrier
Resolver
Registry adapter
CONSUMER
role view
PARTNER
role view
REPAIR / RECYCLE
role view
AUTHORITY
role view
Cross-cutting controls: identity governance | security | privacy | trade secrets | backup | service continuity | observability
Keep the control plane modular so product semantics, hosting and experiences can change independently.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://cirpass2.eu/project-results/
- https://single-market-economy.ec.europa.eu/dpp-registry_en
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 21
DATA MODEL
A canonical product graph connects identity, composition, evidence and lifecycle events
Each published fact needs an owner, source, validity period, granularity and proof status.
Sources:
ESPR | Battery Pass | IDTA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
21
CANONICAL PRODUCT GRAPH
One governed relationship model
IDENTITY
Product, operator, facility, model, batch, item
COMPOSITION
BOM, materials, substances, recycled content
SUPPLY + EVIDENCE
Supplier, chain of custody, issuer, document
SUSTAINABILITY
Footprint, durability, repairability, circularity
LIFECYCLE
Manufacture, sale, repair, reuse, recycling
COMPLIANCE
Rules, declarations, approvals, authority status
Every fact carries
owner | source | granularity | validity | evidence | access class
Model the relationships first; the human-readable passport is only one projection of the graph.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://thebatterypass.eu/battery-pass/materials/
- https://industrialdigitaltwin.org/wp-content/uploads/2026/05/IDTA-02099-1_Submodel-Digital-Product-Passport-Part-1.pdf
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 22
IDENTITY & CARRIER
Choose identifiers and carriers for persistence, not campaign convenience
Open identifiers, resolvers and replaceable destinations avoid relabelling and reduce vendor lock-in.
Sources:
EN 18219 | EN 18220 | GS1 Digital Link
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
22
QR / DATA MATRIX
Strength
Low cost, camera-readable, broad consumer reach
Watch
Durability, print quality and copy risk
Default where physical context permits
NFC / RFID
Strength
Tap or machine read, item-level and industrial workflows
Watch
Cost, reader availability and lifecycle durability
Use for high-value or operational cases
DIGITAL WATERMARK
Strength
Invisible or integrated visual carrier
Watch
Detection ecosystem and persistence must be proven
Use selectively after standards fit
IDENTITY RULE
Encode a persistent identifier that can resolve to changing destinations without changing the physical carrier.
A campaign URL is not an identity strategy; use open identifiers, resolver portability and clear granularity rules.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
- https://ref.gs1.org/standards/digital-link/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 23
REGISTRY FLOW
The EU Registry indexes passports; it does not replace the product-data layer
Economic operators register identifiers and metadata while detailed passport data remains decentralised.
Sources:
European Commission DPP Registry | ESPR
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
23
1
ASSIGN
Economic operator assigns the product identifier and carrier.
2
ASSEMBLE
DPP control plane validates and publishes the detailed record.
3
REGISTER
Identifier and required metadata are submitted to the EU Registry.
4
RESOLVE
A scan or system request finds the appropriate passport endpoint.
5
AUTHORISE
Policy returns the audience-specific data view and logs access.
REGISTRY BOUNDARY
The Registry stores identifiers, registration data and high-level metadata, not the full detailed passport record.
Registry integration is essential, but enterprise data ownership and hosting remain with the economic operator and its providers.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://single-market-economy.ec.europa.eu/dpp-registry_en
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 24
ACCESS & TRUST
Policy-as-code should control who sees what, why and for how long
Role, purpose, consent, legitimate interest, evidence status and audit logging belong in the access model.
Sources:
ESPR | Battery Regulation | Data Act | CRA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
24
Identity and role
Purpose and legal basis
Product and jurisdiction
Data classification
Consent or legitimate interest
Evidence status and expiry
POLICY-AS-CODE ENGINE
Evaluate audience, purpose, product rule, data sensitivity and evidence status at request time.
Return only the allowed view and obligations.
Public view
Partner view
Repair or recycle view
Authority view
Denied or redacted
Logged and monitored
Trust services
Authentication | verifiable evidence | integrity | audit log | backup | incident response
Access decisions must be inspectable and repeatable, especially where trade secrets and legitimate-interest data intersect.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://eur-lex.europa.eu/eli/reg/2023/1542/oj
- https://eur-lex.europa.eu/eli/reg/2023/2854/oj
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=legissum:4797302
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 25
RELEASE ROADMAP
Scale in releases: compliant minimum first, automation and value use cases second
A portfolio rollout can reach full candidate coverage by H1 2029 while the regulated battery cohort closes first.
Sources:
SCULTRA editable roadmap model
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
25
Candidate portfolio coverage
100%
75%
50%
25%
0%
5%
20%
45%
70%
90%
100%
H2 26
H1 27
H2 27
H1 28
H2 28
H1 29
RELEASE LOGIC
H2 2026
Foundation
5%
H1 2027
Battery close
20%
H2 2027
Supplier scale
45%
2028
Portfolio engine
70 to 90%
H1 2029
Industrialised
100%
The battery cohort reaches 100% in H1 2027; broader coverage is a reusable platform rollout, not a legal deadline.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 26
BUILD-BUY-CONTROL
Buy orchestration selectively, but retain identity, semantics and evidence control
A modular contract preserves portability across product acts, service providers and user experiences.
Sources:
ESPR no-lock-in requirement | CIRPASS-2 | SCULTRA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
26
RETAIN CONTROL
Buyer-owned decisions
Product identity policy
Canonical semantics
Evidence acceptance rules
Audience and access policy
Data ownership and exit rights
BUY + CONFIGURE
Platform capabilities
Passport lifecycle workflow
Registry adapter and resolver
Storage and backup service
APIs, portal and monitoring
Rules and release automation
PARTNER
Ecosystem delivery
Supplier onboarding
LCA and conformity evidence
Carrier and label production
Systems integration
Security and assurance testing
The lowest-regret contract buys speed while preserving the buyer's identity, semantics, evidence and portability control.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://cirpass2.eu/project-results/
- https://eur-lex.europa.eu/legal-content/EN/ALL/?uri=intcom:Ares(2024)8031852
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 27
PRODUCT PATTERNS
Granularity and lifecycle cadence change the design by product group
A serialised battery, garment style, batch material and long-lived industrial asset need different publication patterns.
Sources:
Battery Regulation | ESPR | Battery Pass | IDTA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
27
Product pattern
Planning granularity
Lifecycle cadence
Critical data challenge
Architecture implication
Specified battery
Individual battery
Manufacture, use, state, repair, second life
Dynamic performance and tiered access
Event-capable record with durable identity
Textile or apparel
Model, batch or item to be defined
Design, manufacture, sale, care, resale
Multi-tier material and process traceability
High-volume supplier capture and consumer view
Industrial equipment
Model, batch or serial asset
Engineering change, service, retrofit, end of life
BOM, configuration and service alignment
PLM and service integration, AAS fit
Material or component
Batch or lot
Production, transfer, transformation
Chain of custody and confidentiality
Selective disclosure and mass-balance logic
Do not force every product through one granularity or lifecycle-update pattern.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2023/1542/oj
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://thebatterypass.eu/battery-pass/materials/
- https://industrialdigitaltwin.org/wp-content/uploads/2026/05/IDTA-02099-1_Submodel-Digital-Product-Passport-Part-1.pdf
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 28
INTEROPERABILITY
The standards stack is usable, but two decisions and product semantics still evolve
Six harmonised standards now cover protocols, identifiers, carriers, storage, APIs and system interoperability.
Sources:
Commission Implementing Decision (EU) 2026/1736
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
28
EN 18216
Data exchange protocols
EN 18219
Unique identifiers
EN 18220
Data carriers
EN 18221
Storage, archiving and persistence
EN 18222
Lifecycle and search APIs
EN 18223
System interoperability
STATUS
Six harmonised standards are published. The Commission timeline indicates two remaining decisions in September 2026; product semantics still arrive by applicable act.
Adopt the harmonised interface stack now, but isolate evolving product content in configuration and semantic mappings.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
- https://single-market-economy.ec.europa.eu/news/digital-product-passport-registry-now-live-2026-07-20_en
- https://industrialdigitaltwin.org/wp-content/uploads/2026/05/IDTA-02099-1_Submodel-Digital-Product-Passport-Part-1.pdf
- https://ref.gs1.org/standards/digital-link/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 29
03
Vendor & Delivery Ecosystem
Which capabilities sit with enterprise platforms, DPP specialists, traceability providers, data spaces and implementation partners.
SCULTRA REPORT SERIES
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
29
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 30
VALUE CHAIN
The delivery stack spans data creation, exchange, orchestration and verification
No single software layer fixes weak source data or missing supplier participation.
Sources:
Official vendor disclosures | SCULTRA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
30
1
CREATE
Engineering, compliance, supplier and lifecycle facts
2
VERIFY
Evidence, issuer, validity and conformity
3
EXCHANGE
Supplier requests, data spaces and APIs
4
ORCHESTRATE
Canonical model, rules and release workflow
5
IDENTIFY
Persistent ID, carrier and resolver
6
REGISTER
EU identifier and required metadata
7
SERVE
Audience-specific experiences and monitoring
Reality check
A DPP vendor can orchestrate the record, but the buyer and suppliers still create, own and prove most of the data.
Source-data work and operating ownership should be funded as first-class workstreams, not left to system integration.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://www.sap.com/blogs/espr-and-digital-product-passports
- https://www.siemens.com/en-gb/industries/batteries/battery-passport/
- https://www.circularise.com/dpp-for-espr
- https://trustrace.com/solutions/digital-product-passport-dpp-compliance
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 31
VENDOR ARCHETYPES
Vendor fit depends on where the buyer's data and operational complexity already sit
Enterprise suites, industrial platforms, DPP specialists and sector traceability providers solve different parts of the problem.
Sources:
Official vendor product pages | SCULTRA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
31
ENTERPRISE SUITE
SAP
Deep ERP, compliance and business-network integration
Watch DPP completeness and resolver portability
INDUSTRIAL PLATFORM
Siemens | Dassault Systemes
PLM, engineering, digital twin and industrial lifecycle context
Watch cross-enterprise supplier capture
DPP + IDENTITY SPECIALIST
Circularise | Kezzler | Minespider
Purpose-built passports, identity, traceability and selective sharing
Watch source-system depth and sector fit
SECTOR TRACEABILITY
TrusTrace | OPTEL | iPoint
Supplier data, chain of custody and compliance workflows
Watch horizontal portability and platform overlap
Start from the buyer's incumbent data stack and hardest product group, then select the missing capabilities.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://www.sap.com/blogs/espr-and-digital-product-passports
- https://www.siemens.com/en-gb/industries/batteries/battery-passport/
- https://kezzler.com/solutions/compliance/
- https://trustrace.com/solutions/digital-product-passport-dpp-compliance
- https://www.ipoint-systems.com/resources/projects/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 32
VENDOR LANDSCAPE
A credible longlist spans enterprise, industrial and specialist platforms
The longlist includes SAP, Siemens, Dassault Systemes, Circularise, Kezzler, TrusTrace, OPTEL, iPoint and Minespider.
Sources:
Official company disclosures
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
32
ENTERPRISE + PLM
SAP
Dassault Systemes
System-of-record depth
INDUSTRIAL DPP
Siemens DPP4.0
iPoint
Industrial lifecycle
DPP + IDENTITY
Circularise
Kezzler
Minespider
Identity and materials
SECTOR TRACEABILITY
TrusTrace
OPTEL
Supplier and sector depth
This is a capability landscape, not an exhaustive market map or vendor ranking.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://www.sap.com/blogs/espr-and-digital-product-passports
- https://www.siemens.com/en-gb/industries/batteries/battery-passport/
- https://www.3ds.com/sustainability/circular-economy/digital-product-passport
- https://www.circularise.com/dpp-for-espr
- https://kezzler.com/solutions/compliance/
- https://trustrace.com/solutions/digital-product-passport-dpp-compliance
- https://www.optelgroup.com/en/solution/digital-product-passport/
- https://www.ipoint-systems.com/resources/projects/
- https://www.minespider.com/platform
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 33
VENDOR SCORECARD
No vendor leads every system-of-record, traceability, identity and sector dimension
Select a composable coalition and score it against the buyer's incumbent stack, product groups and data-sovereignty needs.
Sources:
Official product pages | SCULTRA assessment
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
33
Vendor
Archetype
Integration
Orchestration
Traceability
Identity
Interop
Sector fit
Data control
Weighted
SAP
Enterprise
5
4
4
3
4
5
4
4.20
Siemens
Industrial
4
5
4
4
4
5
4
4.35
Circularise
Specialist
3
4
5
4
5
4
4
4.15
Kezzler
Identity
3
4
5
5
5
4
4
4.25
TrusTrace
Sector
3
4
5
5
5
5
3
4.30
Minespider
Materials
3
4
5
4
5
4
5
4.25
Illustrative weights: integration 15% | orchestration 20% | traceability 15% | identity 10% | interoperability 15% | sector fit 15% | deployment and data control 10%
Scores are directional. Require architecture tests, customer references, data-portability proof and commercial evidence before selection.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://www.sap.com/blogs/espr-and-digital-product-passports
- https://www.siemens.com/en-gb/industries/batteries/battery-passport/
- https://www.circularise.com/dpp-for-espr
- https://kezzler.com/solutions/compliance/
- https://trustrace.com/solutions/digital-product-passport-dpp-compliance
- https://www.optelgroup.com/en/solution/digital-product-passport/
- https://www.ipoint-systems.com/resources/projects/
- https://www.minespider.com/platform
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 34
REFERENCE DEPLOYMENTS
Pilots are proving architecture and data exchange, not universal compliance
CIRPASS-2, Battery Pass, FAIR PV, Trace4Value and Catena-X provide patterns to reuse and questions to diligence.
Sources:
EU-funded projects | official case studies
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
34
CIRPASS-2
Cross-sector
Reference architecture, open test environment and at-scale pilots
Reuse the interfaces and risk questions
Battery Pass
Batteries
Data attributes, conformity guidance and demonstrators
Use as the first implementation pattern
FAIR PV
Solar modules
Dynamic DPP, ontology and selective supplier disclosure
Current-condition data matters for circularity
Trace4Value
Textiles
Open data protocol and working garment passports
Supplier data collection is the critical path
Catena-X
Automotive
AAS models, data-space identity and sovereign exchange
Data spaces can complement the DPP control plane
Treat pilots as evidence for specific patterns, not proof that one solution satisfies every product act.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://cirpass2.eu/project-results/
- https://thebatterypass.eu/battery-pass/materials/
- https://www.circularise.com/case-studies/building-a-transparent-solar-future-how-circularise-and-fair-pv-pioneered-circularity-with-digital-product-passports
- https://trustrace.com/solutions/digital-product-passport-dpp-compliance
- https://catena-x.net/fileadmin/user_upload/Standard-Bibliothek/Update_Maerz_2024/CX-0103-AspectModelDigitalProductPassport-v1.1.0.pdf
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 35
STANDARDS EVOLUTION
Standards have crossed the execution threshold, while product rules continue to arrive
Use harmonised interfaces now and isolate configurable product semantics from the platform core.
Sources:
European Commission | EUR-Lex | GS1 | IDTA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
35
2024
ESPR framework
System requirements and Registry mandate
2025
Working Plan + CIRPASS
Portfolio priorities and reference architecture
JUL 2026
Registry + 6 standards
Execution infrastructure becomes usable
SEP 2026*
2 decisions indicated
Remaining standards on access and security expected
Q4 2026*
Iron and steel + battery access
Product-specific rules continue
2027*
Batteries + service providers + product acts
Operational scale and certification questions
* Indicative Commission timeline. Verify delegated and implementing acts before contract award or external publication.
Design for standards compliance now, and for semantic and service-provider change later.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport_en
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
- https://ref.gs1.org/standards/digital-link/
- https://industrialdigitaltwin.org/wp-content/uploads/2026/05/IDTA-02099-1_Submodel-Digital-Product-Passport-Part-1.pdf
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 36
SOURCING ROUTE
Use a two-stage selection: architecture proof, then regulated-product pilot
Down-select vendors on interoperability evidence before negotiating scale, service and commercial terms.
Sources:
SCULTRA sourcing framework | EU no-lock-in requirement
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
36
01
ARCHITECTURE RFI
4 to 6 weeks
Test standards, identity, hosting, APIs, security, backup and exit evidence
02
SANDBOX PROOF
4 to 6 weeks
Connect two source systems, one supplier flow, one carrier and the Registry test environment
03
REGULATED PILOT
8 to 16 weeks
Publish the minimum compliant record and pass acceptance, access and persistence tests
04
FRAMEWORK AWARD
12 to 36 months
Scale product families through modular services, price bands, release gates and exit rights
Stop or reconfigure at each evidence gate
Do not negotiate enterprise scale before the vendor proves interoperability, persistence and regulated-product execution.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://eur-lex.europa.eu/legal-content/EN/ALL/?uri=intcom:Ares(2024)8031852
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 37
DELIVERY COALITION
A bankable program requires seven owners on one release plan
Product compliance, master data, engineering, procurement, sustainability, IT security and suppliers share the outcome.
Sources:
SCULTRA operating model | ESPR
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
37
DPP RELEASE OWNER
Accountable for product record and gate approval
PRODUCT COMPLIANCE
Scope and conformity
MASTER DATA
Identity and ownership
ENGINEERING
BOM and change
PROCUREMENT
Supplier data contract
SUSTAINABILITY
Footprints and claims
IT + SECURITY
Architecture and controls
SUPPLIERS
Primary data and evidence
One integrated release plan should align product decisions, data readiness, supplier commitments and technical milestones.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport/economic-operators_en
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 38
BUYER JOURNEY
Commercial leverage is highest before identity and data models become proprietary
Define architecture principles, exit rights and evidence tests before a platform pilot shapes the target state.
Sources:
SCULTRA sourcing framework | ESPR
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
38
1
PRINCIPLES
Define identity, semantics, data control and exit
2
EVIDENCE
Map sources, suppliers, proof and gaps
3
PROOF
Run sandbox integration and standards tests
4
PILOT
Publish regulated cohort and operate controls
5
SCALE
Add product rules and value use cases
Commercial leverage
HIGHEST
LOCK-IN RISES
Set the control points before a pilot makes one vendor's data model and identity choices expensive to unwind.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 39
RISK ALLOCATION
Put persistence, portability and data quality into the contract
Service continuity, backup, change handling, access control, audit evidence and exit migration need measurable acceptance criteria.
Sources:
ESPR | DPP service-provider initiative | CRA
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
39
Risk
Primary owner
Contract control
Acceptance evidence
Data is incomplete or stale
Buyer + supplier
Field owner, validity and remediation SLA
Completeness and age dashboard
Identifier or resolver lock-in
Platform provider
Open identifier, resolver and export rights
Successful alternate resolution test
Provider outage or exit
Service provider
Backup, escrow, RTO, RPO and migration support
Restore and exit rehearsal
Access leaks confidential data
Buyer + provider
Policy matrix, least privilege and audit
Role tests and access-log review
Regulatory change requires rework
Buyer + provider
Configuration commitment and change pricing
New product rule without code fork
Lifecycle events do not update
Buyer systems + integrator
Event interfaces and monitoring SLA
Change-to-publication reconciliation
Allocate each risk to the party that can control it, then make acceptance evidence part of payment and scale gates.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://eur-lex.europa.eu/legal-content/EN/ALL/?uri=intcom:Ares(2024)8031852
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=legissum:4797302
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 40
04
Implementation Strategy
Where to start, how to structure the operating model and what to validate during the first 90 days.
SCULTRA REPORT SERIES
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
40
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 41
WHERE TO START
Start with one regulated cohort and one reusable enterprise use case
Prioritise batteries where applicable; otherwise use a data-rich product family that exercises suppliers, evidence and lifecycle updates.
Sources:
EU timeline | SCULTRA strategy
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
41
HIGH
REGULATORY URGENCY
LOW
REMEDIATE THEN PILOT
START NOW
PROVE VALUE USE CASE
MONITOR + MAP
Specified batteries
Textiles
Industrial equipment
Furniture
Material batch
LOW
DATA READINESS
HIGH
Use a regulated cohort where applicable; otherwise select a data-rich family that exercises suppliers, evidence and updates.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport_en
- https://eur-lex.europa.eu/eli/reg/2023/1542/oj
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport/economic-operators_en
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 42
HOW TO WIN
Govern the data product before scaling the passport experience
Keep the canonical model, identifiers, evidence rules and exit rights under buyer control while configuring product-specific content.
Sources:
EU law | standards | SCULTRA strategy
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
42
01
OWN IDENTITY
Persistent identifiers, granularity and resolver portability
02
GOVERN SEMANTICS
Canonical model, product-rule configuration and field ownership
03
PROVE EVIDENCE
Issuer, source, validity, assurance level and approval trail
04
POLICY THE ACCESS
Audience, purpose, privacy, trade secret and logging rules
05
DESIGN FOR EXIT
Backup, export, restore, alternate resolver and migration support
06
OPERATE RELEASES
Change events, quality gates, monitoring and incident response
Keep control of the durable assets, buy configurable execution capability and measure every release.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
- https://ref.gs1.org/standards/digital-link/
- https://cirpass2.eu/project-results/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 43
90-DAY SPRINT
A 90-day readiness sprint can convert uncertainty into an executable pilot
Confirm scope, map data and identity, prove the architecture, assess vendors and approve a stage-gated implementation.
Sources:
SCULTRA recommended next steps
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
43
DAYS 1 TO 30
Scope and diagnose
Confirm applicable products and accountable operator
Map identifiers, systems, suppliers and evidence
Set architecture and no-lock-in principles
Baseline readiness and cost model
DAYS 31 TO 60
Design and prove
Create canonical data and access model
Connect two source systems and one supplier
Test carrier, resolver and Registry sandbox
Assess vendor architecture and exit evidence
DAYS 61 TO 90
Select and mobilise
Approve target architecture and operating model
Select regulated pilot and vendor coalition
Negotiate stage gates, service levels and exit
Launch pilot backlog and control dashboard
The 90-day decision should require a proven architecture, named pilot cohort, evidence-based vendor shortlist and funded control owner.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport_en
- https://single-market-economy.ec.europa.eu/dpp-registry_en
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 44
CLOSING
Treat DPP as market-access infrastructure
Use the editable model to replace illustrative inputs with the product portfolio, data evidence, supplier readiness and vendor proposals.
Sources:
Evidence base listed on this slide
SCULTRA SERVICES
EU DIGITAL PRODUCT PASSPORT & PRODUCT TRACEABILITY
44
FINAL VIEW
Treat DPP as market-access infrastructure.
The Registry and standards are ready enough to act. The enterprise constraint is whether product identity, evidence and lifecycle data can be governed at scale.
Recommended architecture
Federated source data, buyer-controlled identity and semantics, modular passport orchestration, policy-based access, durable backup and evidence-gated releases.
Primary evidence base
1
Regulation (EU) 2024/1781
2
Regulation (EU) 2023/1542
3
Commission DPP portal and Registry
4
Decision (EU) 2026/1736
5
CIRPASS-2 reference architecture
6
GS1 Digital Link and IDTA AAS
7
Official vendor product pages
8
SCULTRA readiness and TCO model
Next step: replace illustrative inputs with the product portfolio, evidence gaps, supplier readiness and vendor proposals, then run the 90-day sprint.
Notes: Illustrative SCULTRA report. Regulatory facts are current to 8 August 2026. Verify time-sensitive delegated and implementing acts before external publication. Portfolio, readiness, cost and vendor values are editable SCULTRA assumptions.
[Sources]
- https://eur-lex.europa.eu/eli/reg/2024/1781/oj
- https://eur-lex.europa.eu/eli/reg/2023/1542/oj
- https://single-market-economy.ec.europa.eu/single-market/digital-product-passport_en
- https://single-market-economy.ec.europa.eu/dpp-registry_en
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32026D1736
- https://cirpass2.eu/project-results/
- https://ref.gs1.org/standards/digital-link/
- https://industrialdigitaltwin.org/wp-content/uploads/2026/05/IDTA-02099-1_Submodel-Digital-Product-Passport-Part-1.pdf
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]