## Slide 1
ILLUSTRATIVE FLAGSHIP REPORT
Solid-State Batteries &
Next-Generation Energy Storage
Technology Landscape, Patent Signals and Commercialization Strategy
Illustrative report | August 2026
Technology scouting | Patent analytics | Supplier assessment | Sourcing strategy
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
01
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 2
EXECUTIVE SUMMARY
The race is shifting from chemistry claims to manufacturable interfaces
Five findings define where value, IP and sourcing attention should concentrate.
Sources:
WIPO | IEA | Nature Energy | company evidence | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
02
1
The commercial race is now a manufacturing race
Materials performance is necessary, but pilot yield, thin-layer uniformity and repeatable cell assembly determine time to market.
2
Interfaces are the main control point
Contact loss, interphase growth, voids and lithium filaments link chemistry to mechanical design and formation protocol.
3
Early markets will be segmented
Premium EVs, aviation, defense and robotics can monetize energy density, safety or runtime before mass-market applications.
4
Patent value is shifting into the production system
Recent claims increasingly combine composition with membrane formation, stack architecture, pressure and process control.
5
The right strategy is selective ownership
Own application-specific interfaces, validation data and system design; partner for chemistry breadth and capital-intensive scale.
EXECUTIVE DECISIONS
01
Where to focus
Interfaces, thin electrolyte films, formation, pressure architecture and in-line quality control.
02
What to verify
Automotive-format cells, test conditions, external validation, pilot throughput, yield and supply readiness.
03
How to engage
Stage partnerships around evidence gates, data access, claim mapping and a defined route to industrialization.
INSIGHT
The strongest opportunity is not a universal chemistry bet. It is control of a manufacturable interface for a valuable application.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html
- https://www.iea.org/reports/global-ev-outlook-2025/electric-vehicle-batteries
- https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies
- https://www.nature.com/articles/s41560-023-01208-9
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation] [Sources] - https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html - https://www.iea.org/reports/global-ev-outlook-2026/electric-vehicle-batteries - https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies [/Sources]

## Slide 3
EXECUTIVE CONTEXT
Technical momentum is real, but production readiness still trails the narrative
Three signals frame the opportunity and the commercialization gap.
Sources:
WIPO 2025 | IEA 2025 | IEA Global EV Outlook 2025
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
03
TRL 6
Automotive all-solid-state readiness
IEA assessed the technology at large-pilot stage in 2024, with vehicle validation now emerging.
2,033
Published patent families in 2023
WIPO reports an increase from 290 in 2010, a sevenfold rise across the period.
1%
Share of committed battery capacity
IEA estimates solid-state projects at only 1% of installed, under-construction or final-investment-decision capacity.
TECHNOLOGY
Pilot-stage
Performance is credible at cell level, but pack and factory evidence remains uneven.
PATENTS
Accelerating
Crowding is rising in materials while new claims form around process and integration.
CAPACITY
Constrained
Industrial scale remains the scarce asset and the main source of commercialization risk.
INSIGHT
Momentum is real, but the investment signal is still evidence of scale-up, not the solid-state label itself.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html
- https://www.iea.org/reports/global-ev-outlook-2025/electric-vehicle-batteries
- https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 4
REPORT GUIDE
Contents
A decision-oriented view of technology, ecosystem, patents and strategic action.
Sources:
SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
04
01
Technology Landscape
Architecture, electrolytes, interfaces, manufacturing and readiness
Slides 05 to 17
02
Market & Ecosystem
Applications, economics, regions, companies, partnerships and qualification
Slides 18 to 28
03
Patent Landscape
Activity, geography, claim taxonomy, public families and white spaces
Slides 29 to 39
04
Strategy & Sourcing
Build-buy-partner choices, diligence, 90-day sprint and caveats
Slides 40 to 44
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 5
01
Technology Landscape
Where performance is created, where cells fail and what manufacturing must solve.
SCULTRA REPORT SERIES
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
05
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 6
TECHNOLOGY LANDSCAPE
Solid-state is a spectrum, not one product category
Semi-solid, quasi-solid and all-solid-state architectures carry different risk, cost and qualification paths.
Sources:
IEA Global EV Outlook 2025 | Nature Energy
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
06
01
SEMI-SOLID
Liquid-rich
Gel or suspension reduces leakage and may improve energy density while retaining liquid transport.
Nearer term
02
QUASI-SOLID
Hybrid interface
A solid or gel matrix with residual liquid can ease contact and processing challenges.
Bridge architecture
03
ALL-SOLID-STATE
Solid separator
The solid electrolyte performs ion transport and separator functions, enabling new anodes.
Highest upside, highest gate
Less architectural change
More interface and manufacturing burden
INSIGHT
Commercial comparisons should begin with electrolyte state, anode architecture and test conditions, not the product label.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.iea.org/reports/global-ev-outlook-2025/electric-vehicle-batteries
- https://www.nature.com/articles/s41560-023-01208-9
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 7
TECHNOLOGY LANDSCAPE
The solid electrolyte changes both the energy pathway and the failure modes
Higher-energy anodes become possible, but the cell must manage solid-to-solid contact throughout life.
Sources:
IEA 2026 | Nature Energy | SCULTRA illustrative visual
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
07
ILLUSTRATIVE ARCHITECTURE
1
Current collectors
Electron pathway and mechanical support
2
Composite cathode
Active material, conductor and solid electrolyte must maintain percolation
3
Solid electrolyte
Carries lithium ions and separates electrodes
4
Lithium-metal interface
Plating uniformity, void control and interphase stability determine life
INSIGHT
The electrolyte removes flammable liquid and can enable lithium metal, but it also converts wetting into a persistent contact-management problem.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.iea.org/reports/global-ev-outlook-2026/electric-vehicle-batteries
- https://www.nature.com/articles/s41560-023-01208-9
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation] [Sources] - https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html - https://www.iea.org/reports/global-ev-outlook-2026/electric-vehicle-batteries - https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies [/Sources]

## Slide 8
TECHNOLOGY LANDSCAPE
No electrolyte family wins every performance and manufacturing dimension
Sulfides lead on conductivity and processability, while oxides, polymers, halides and composites solve different constraints.
Sources:
Nature Reviews Materials | Communications Materials | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
08
LOW
HIGH ROOM-TEMPERATURE CONDUCTIVITY
HIGH
LOW PROCESSABILITY
HIGH PROCESSABILITY
POLYMER
Flexible, lower ambient conductivity
OXIDE
Stable, brittle, high-temperature processing
SULFIDE
High conductivity, moisture sensitive
HALIDE
Cathode compatibility, emerging scale
COMPOSITE
Balance through engineered phases
INSIGHT
Sulfides are strong candidates for high-energy EV cells, but composites and application-specific hybrids may offer the fastest route to robust production.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nature.com/articles/s41578-019-0165-5
- https://www.nature.com/articles/s43246-024-00482-8
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation] [Sources] - https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html - https://www.iea.org/reports/global-ev-outlook-2026/electric-vehicle-batteries - https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies [/Sources]

## Slide 9
TECHNOLOGY LANDSCAPE
Chemistry choice is a trade between conductivity, stability and factory conditions
The winning formulation depends on the anode, cathode, process window and application.
Sources:
Nature Reviews Materials | Nature Energy | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
09
ELECTROLYTE
IONIC CONDUCTIVITY
PROCESSABILITY
CHEMICAL STABILITY
MOISTURE TOLERANCE
PRIMARY SCALE-UP GATE
Sulfide
High
High
Medium
Low
Dry-room control, gas risk, interface coatings
Oxide
Medium
Low
High
High
Brittleness, sintering and interfacial resistance
Polymer
Low to medium
High
Medium
High
Ambient conductivity and high-voltage stability
Halide
Medium to high
Medium
High at cathode
Low to medium
Cost, reduction stability and supply maturity
Composite
Design dependent
Medium to high
Design dependent
Medium
Phase compatibility and reproducible formulation
INSIGHT
A sourcing decision should require an electrolyte-specific manufacturing model, not a generic solid-state cost curve.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nature.com/articles/s41578-019-0165-5
- https://www.nature.com/articles/s41560-023-01208-9
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation] [Sources] - https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html - https://www.iea.org/reports/global-ev-outlook-2026/electric-vehicle-batteries - https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies [/Sources]

## Slide 10
TECHNOLOGY LANDSCAPE
Lithium-metal and anode-free designs move value into formation and interface control
Eliminating graphite creates energy upside but raises requirements for uniform plating, current density and surface quality.
Sources:
Nature Energy | QuantumScape | Samsung SDI
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
10
01
LITHIUM-METAL FOIL
Lithium is introduced as a thin foil
High initial lithium inventory
Requires thin, uniform foil handling
Can simplify formation assumptions
02
ANODE-FREE
Lithium plates from the cathode during charge
Highest packaging efficiency
Formation controls lithium inventory
Current collector surface is critical
03
SILICON COMPOSITE
High-capacity host replaces graphite-rich anode
Less radical factory change
Large volume expansion
Hybrid route to higher energy density
FORMATION BECOMES PRODUCT DESIGN
INSIGHT
Anode-free architectures remove a material and a process step, but transfer risk into formation, current-collector engineering and irreversible lithium loss.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nature.com/articles/s41560-023-01208-9
- https://www.quantumscape.com/quantumscape-releases-next-generation-solid-state-battery-separator-equipment-cobra/
- https://news.samsungsdi.com/global/articleView?seq=203
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation] [Sources] - https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html - https://www.iea.org/reports/global-ev-outlook-2026/electric-vehicle-batteries - https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies [/Sources]

## Slide 11
TECHNOLOGY LANDSCAPE
Most practical failures originate at buried interfaces
Voids, contact loss, interphase growth, cracking and filament formation reinforce one another during cycling.
Sources:
Nature Reviews Materials | DST-IISc | Nature Energy
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
11
BURIED INTERFACE
Contact, chemistry and mechanics evolve together
VOID FORMATION
Lithium removal creates local gaps
CONTACT LOSS
Volume change breaks ion pathways
INTERPHASE GROWTH
Side reactions increase resistance
CRACKING
Brittle layers concentrate stress
CURRENT HOTSPOTS
Non-uniform flux accelerates damage
FILAMENTS
Lithium penetrates defects or cracks
INSIGHT
Interface life should be evaluated under realistic current density, pressure, temperature and areal capacity, not by cycle count alone.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.nature.com/articles/s41578-019-0157-5
- https://dst.gov.in/dst-iisc-energy-storage-platform-moves-towards-enabling-fast-charging-solid-state-batteries
- https://www.nature.com/articles/s41560-023-01208-9
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation] [Sources] - https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html - https://www.iea.org/reports/global-ev-outlook-2026/electric-vehicle-batteries - https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies [/Sources]

## Slide 12
TECHNOLOGY LANDSCAPE
Pressure is part of the cell architecture, not just a laboratory test condition
Too little pressure loses contact; too much adds mass, damages layers and complicates the pack.
Sources:
IEA battery innovation analysis | Nature Energy | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
12
ILLUSTRATIVE PRESSURE WINDOW
LOW
STACK PRESSURE
HIGH
Contact loss
Voids and rising impedance
Operating window
Stable contact with manageable pack burden
Over-compression
Damage, creep and heavy hardware
PACK CONSEQUENCES
Cell hardware
Springs, frames or compliant layers maintain pressure as thickness changes.
Energy density
Compression hardware and lower packing efficiency can offset cell-level gains.
Controls
Pressure sensing and state estimation may become safety and warranty inputs.
Claims
Mechanical architecture and pressure-control systems are defensible integration terrain.
INSIGHT
A cell that needs high external pressure may still succeed, but only if pack-level mass, volume, cost and control are included in the evidence.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies
- https://www.nature.com/articles/s41560-023-01208-9
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation] [Sources] - https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html - https://www.iea.org/reports/global-ev-outlook-2026/electric-vehicle-batteries - https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies [/Sources]

## Slide 13
TECHNOLOGY LANDSCAPE
Scale-up requires a new process window inside a familiar battery factory
Mixing, coating, densification, lamination, dry-room control, formation and inspection all change.
Sources:
Honda demonstration line | QuantumScape Cobra | Nature Energy
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
13
1
SYNTHESIZE
Electrolyte purity and particle control
2
MIX
Composite ionic and electronic networks
3
COAT
Thin, uniform layers at useful speed
4
DENSIFY
Contact without damage or closed porosity
5
LAMINATE
Bond layers and control alignment
6
FORM
Create stable lithium interface
7
INSPECT
Detect defects before costly assembly
Dry environment
Sulfide moisture sensitivity can tighten dew-point and safety requirements.
New metrology
Subsurface cracks, thickness variation and interface defects require in-line inspection.
Formation data
The first cycles become a manufacturing-control and product-design step.
INSIGHT
The practical advantage goes to architectures that reuse high-throughput coating and assembly assets without carrying laboratory-only conditions into the pack.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://global.honda/en/newsroom/news/2024/c241121eng.html
- https://www.quantumscape.com/quantumscape-releases-next-generation-solid-state-battery-separator-equipment-cobra/
- https://www.nature.com/articles/s41560-023-01208-9
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 14
TECHNOLOGY LANDSCAPE
Yield, thin-layer uniformity and moisture control are the main economic bottlenecks
A high-performing material does not become a product until defects are controlled at speed and area.
Sources:
Honda | QuantumScape | Communications Materials | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
14
BOTTLENECK
WHY IT HITS YIELD
EVIDENCE TO REQUEST
STRATEGIC IMPACT
Electrolyte thickness
Pinholes and local resistance
Area distribution, defect rate, line speed
Very high
Layer adhesion
Delamination during cycling
Peel data, impedance growth, pressure dependence
High
Moisture exposure
Sulfide degradation and gas risk
Dew point, excursion controls, scrap history
Very high
Lithium uniformity
Hotspots and early shorting
Current-density maps, failure analysis, formation yield
Very high
Particle distribution
Broken ionic or electronic pathways
Batch statistics, mixing window, supplier specs
High
End-of-line inspection
Latent defects escape to costly testing
Coverage, false negatives, correlation to life
High
INSIGHT
A supplier with a credible defect taxonomy and yield-learning loop may be more valuable than one with the highest single-cell energy density.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://global.honda/en/newsroom/news/2024/c241121eng.html
- https://www.quantumscape.com/quantumscape-releases-next-generation-solid-state-battery-separator-equipment-cobra/
- https://www.nature.com/articles/s43246-024-00482-8
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 15
TECHNOLOGY LANDSCAPE
Early adoption will favor applications that monetize energy density and safety
Premium EVs, aviation, defense and robots can tolerate higher cost before mass-market cars and stationary storage.
Sources:
IEA battery innovation analysis | Samsung SDI | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
15
DEFER
PRIORITIZE
AVOID EARLY
PREMIUM BEACHHEAD
LOW WILLINGNESS TO PAY
HIGH WILLINGNESS TO PAY
LOW PERFORMANCE VALUE
HIGH PERFORMANCE VALUE
Premium EV
Aviation
Defense
Humanoid robots
Consumer devices
Mass-market EV
Stationary storage
INSIGHT
The most attractive first markets value compact energy, payload, safety or uninterrupted runtime enough to absorb early manufacturing cost.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies
- https://news.samsungsdi.com/global/articleView?seq=397
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 16
TECHNOLOGY LANDSCAPE
Readiness varies more by architecture than by the solid-state label
Quasi-solid cells are commercializing first; automotive all-solid-state platforms remain in pilot and vehicle-validation stages.
Sources:
IEA Global EV Outlook 2025 | company evidence | SCULTRA assessment
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
16
9
Commercial volume
Established lithium-ion and selected semi-solid cells
7-8
System qualification
Quasi-solid vehicle programs and early fleet validation
6
Large pilot
Automotive all-solid-state cells and pilot manufacturing
4-5
Integrated prototype
New halide, oxide, composite and lithium-metal variants
1-3
Research concept
Novel conductors, coatings and interface mechanisms
SCULTRA VIEW
TRL 6
Large pilot is the right baseline for automotive all-solid-state in 2026, with company-specific exceptions.
INSIGHT
Readiness should be scored at architecture and process level. A material TRL cannot substitute for automotive-format cell and pack evidence.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.iea.org/reports/global-ev-outlook-2025/electric-vehicle-batteries
- https://group.mercedes-benz.com/technology/e-mobility/electric-drive/solid-state-battery-test-car.html
- https://ir.solidpowerbattery.com/investor-relations/investor-news/news-details/2025/BMW-Group-and-Solid-Power-are-Testing-All-Solid-State-Battery-Cells-in-a-BMW-I7/default.aspx
- https://ir.quantumscape.com/node/6616/pdf
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 17
TECHNOLOGY LANDSCAPE
The credible commercialization path is gated by evidence, not announcement dates
Cell samples, vehicle tests, stable pilot yield and qualified supply must precede meaningful volume.
Sources:
Toyota | Samsung SDI | Honda | QuantumScape | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
17
2026
Samples and vehicles
B1 samples, motorcycle and passenger-car test programs, pilot-line learning
2027-28
Initial launches
Targeted premium or limited-volume applications from leading programs
2029-30
Qualification and ramp
Yield, supply and pack architecture determine whether volume expands
2031-32
Segmented scale
Winning architectures broaden where system economics remain attractive
DATES ARE TARGETS, NOT EVIDENCE
INSIGHT
The investable milestone is repeatable yield under commercial test conditions, followed by qualified supply and vehicle-level economics.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://global.toyota/en/newsroom/corporate/39865919.html
- https://news.samsungsdi.com/global/articleView?seq=397
- https://global.honda/en/newsroom/news/2024/c241121eng.html
- https://ir.quantumscape.com/node/6616/pdf
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 18
02
Market & Ecosystem
Where demand, capabilities, partnerships and qualification paths are converging.
SCULTRA REPORT SERIES
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
18
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 19
MARKET & ECOSYSTEM
Solid-state enters a market where incumbent lithium-ion keeps improving
Lower costs, denser packs and faster charging raise the threshold that a new architecture must clear.
Sources:
IEA Global EV Outlook 2026 | IEA innovation analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
19
1.2 TWh
EV battery deployment in 2025
The addressable market is already large and industrialized.
-8%
Average battery price in 2025
Incumbent economics continue to improve while new platforms scale.
>55%
LFP share of EV deployment
Low-cost chemistry raises the threshold for mass-market substitution.
The moving performance threshold
Cell energy
Must survive pack-level overhead
Fast charge
Must hold across life and temperature
Safety
Must reduce system cost, not only pass abuse tests
Cost
Must compete with a learning incumbent
COMMERCIAL TEST
Deliver a system benefit that liquid lithium-ion cannot match at the target launch date.
INSIGHT
Solid-state competes against the next generation of lithium-ion, not today's laboratory baseline.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.iea.org/reports/global-ev-outlook-2026/electric-vehicle-batteries
- https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 20
MARKET & ECOSYSTEM
Near-term economics favor premium segments and constrained form factors
Value comes from range, payload, runtime and safety before it comes from lowest cost per kilowatt-hour.
Sources:
IEA battery innovation analysis | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
20
Application
Value driver
Benefit
Cost tolerance
Entry
Aviation & defense
Payload, safety, endurance
EARLY
Robotics & physical AI
Runtime, compact form factor
EARLY
Premium EV
Range, fast charge, brand value
SELECTIVE
Mass-market EV
Cost, reliability, volume
LATER
Stationary storage
Cycle cost, bankability
NICHE
Benefit and cost-tolerance ratings are directional SCULTRA assessments.
INSIGHT
The first economic wedge is a high-value constraint, not the broadest battery market.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.iea.org/commentaries/how-can-innovation-help-secure-future-battery-markets-and-mineral-supplies
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 21
MARKET & ECOSYSTEM
Asia leads materials and cell scale, while Europe and the United States concentrate vehicle validation
Regional advantage reflects different combinations of incumbents, specialists, public funding and OEM pull.
Sources:
IEA | WIPO | company evidence | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
21
JAPAN
Historical IP depth
Toyota, Honda, Nissan, Idemitsu
Materials, cells, OEM integration
KOREA
Cell incumbent scale
Samsung SDI, SK On
Cell engineering, materials, customers
CHINA
Research and capacity
Broad cell and materials ecosystem
Pilot speed, supply chain, equipment
EUROPE
Vehicle validation
BMW, Mercedes-Benz, VW, ProLogium
OEM test fleets, regulation, scale-up
UNITED STATES
Specialist platforms
QuantumScape, Solid Power, Factorial
IP-led specialists, licensing, pilots
INSIGHT
Regional leadership is complementary: materials and cell scale in Asia, specialist IP in the United States, and vehicle validation in Europe.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.iea.org/reports/global-ev-outlook-2025/electric-vehicle-batteries
- https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html
- https://prologium.com/manufacturing/expansion-roadmap/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 22
MARKET & ECOSYSTEM
The value chain expands around solid-electrolyte precursors, lithium metal and specialized equipment
Materials purity, handling, process equipment and metrology create new supplier dependencies.
Sources:
Toyota-Idemitsu | Solid Power-SK On | Honda | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
22
01
Precursors
High-purity salts, binders, lithium sources
02
Electrolyte
Powder synthesis, particle control, membrane formation
03
Electrodes
Cathode composite, lithium foil or anode-free collector
04
Cell process
Coating, densification, lamination, stack, formation
05
Pack & vehicle
Pressure system, BMS, thermal and crash integration
NEW SUPPLIER DEPENDENCIES
Moisture-sensitive handling
Thin-film equipment
Pressure hardware
In-line defect metrology
Lithium-metal logistics
INSIGHT
Sourcing scope must extend beyond active materials into equipment, metrology, dry-room capability and pack mechanics.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://global.toyota/en/newsroom/corporate/39865919.html
- https://www.solidpowerbattery.com/investor-relations/investor-news/news-details/2024/Solid-Power-and-SK-On-Deepen-Partnership-with-New-Agreements/default.aspx
- https://global.honda/en/newsroom/news/2024/c241121eng.html
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 23
MARKET & ECOSYSTEM
The company landscape is separating into integrated platforms and specialist enablers
No single model dominates: automakers, cell producers, materials firms and IP-led specialists are partnering across layers.
Sources:
Company sources | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
23
INTEGRATED OEM
Toyota
Honda
Nissan
Own cell, process and vehicle learning
CELL INCUMBENT
Samsung SDI
SK On
Scale, quality systems and customers
SPECIALIST PLATFORM
QuantumScape
Solid Power
Factorial
Focused IP and partnership-led scale
MATERIAL ENABLER
Idemitsu
Cathode and equipment partners
Electrolyte supply and process inputs
INSIGHT
Commercialization favors networks that combine proprietary control points with industrial assets and OEM validation.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://global.toyota/en/newsroom/corporate/39865919.html
- https://www.volkswagen-group.com/en/press-releases/powerco-and-quantumscape-announce-landmark-agreement-to-industrialize-solid-state-batteries-18494
- https://www.solidpowerbattery.com/investor-relations/investor-news/news-details/2024/Solid-Power-and-SK-On-Deepen-Partnership-with-New-Agreements/default.aspx
- https://news.samsungsdi.com/global/articleView?seq=397
- https://prologium.com/manufacturing/expansion-roadmap/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 24
MARKET & ECOSYSTEM
Capability depth matters more than a headline energy-density number
Commercial readiness requires cell evidence, process ownership, OEM integration and a credible path to supply.
Sources:
Official company sources | SCULTRA assessment
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
24
Platform
Cell evidence
Process assets
OEM integration
Scale route
Toyota / Idemitsu
Advanced samples
Pilot + electrolyte chain
Internal
Integrated
Honda
Prototype program
Demo line
Internal
Integrated
QuantumScape / PowerCo
24-layer + B samples
Separator equipment
VW / Ducati
License
Solid Power / BMW / SK On
Vehicle + cell pilots
Electrolyte + pilot
BMW
License / supply
Samsung SDI
S-Line program
Cell incumbent
Multiple OEMs
Internal
ProLogium
Pilot + expansion plan
Ceramic platform
Partnered
Owned factories
Evidence descriptions reflect public information and are not directly comparable test results.
INSIGHT
Prioritize repeatable cell data, pilot ownership and a named route to industrialization over one headline metric.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.volkswagen-group.com/en/press-releases/powerco-confirms-results-quantumscapes-solid-state-cell-passes-first-endurance-test-18031
- https://ir.quantumscape.com/node/6616/pdf
- https://global.honda/en/newsroom/news/2024/c241121eng.html
- https://www.solidpowerbattery.com/investor-relations/investor-news/news-details/2026/Solid-Power-Reports-First-Quarter-2026-Results/default.aspx
- https://news.samsungsdi.com/global/articleView?seq=397
- https://group.mercedes-benz.com/technology/e-mobility/electric-drive/solid-state-battery-test-car.html
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 25
MARKET & ECOSYSTEM
Automakers are hedging architectures while building internal validation capability
Toyota and Honda emphasize internal manufacturing; Volkswagen, BMW, Mercedes and Stellantis combine specialist cells with OEM integration.
Sources:
Official OEM and supplier sources
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
25
BUILD INTERNALLY
Toyota | Honda
Own process learning and vehicle integration
LICENSE & INDUSTRIALIZE
Volkswagen / PowerCo | QuantumScape
Pair specialist separator IP with cell-manufacturing scale
CO-DEVELOP & VALIDATE
BMW | Solid Power
Use test vehicles to close cell-to-pack evidence gaps
MULTI-PARTNER HEDGE
Mercedes-Benz | Stellantis and specialists
Preserve optionality across architectures
INSIGHT
OEM strategy is converging on internal validation capability, even when the core cell platform comes from a partner.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://global.toyota/en/newsroom/corporate/39865919.html
- https://global.honda/en/newsroom/news/2024/c241121eng.html
- https://www.volkswagen-group.com/en/press-releases/powerco-and-quantumscape-announce-landmark-agreement-to-industrialize-solid-state-batteries-18494
- https://ir.solidpowerbattery.com/investor-relations/investor-news/news-details/2025/BMW-Group-and-Solid-Power-are-Testing-All-Solid-State-Battery-Cells-in-a-BMW-I7/default.aspx
- https://group.mercedes-benz.com/technology/e-mobility/electric-drive/solid-state-battery-test-car.html
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 26
MARKET & ECOSYSTEM
Partnerships reveal that electrolyte production and vehicle integration are the scarce capabilities
Licensing, joint validation and pilot-line transfer are replacing simple cell-supply relationships.
Sources:
Volkswagen-PowerCo | Solid Power-SK On | Samsung-BMW-Solid Power
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
26
Toyota
Idemitsu
Sulfide electrolyte supply
MATERIAL + SCALE
PowerCo
QuantumScape
Industrialization license
IP + MANUFACTURING
Solid Power
SK On
Electrolyte and cell transfer
MATERIAL + PROCESS
BMW
Solid Power
i7 test vehicle
VALIDATION
Mercedes-Benz
Factorial
Road testing
VALIDATION
INSIGHT
The scarce asset is not only cell supply. It is transferable process knowledge plus application-level evidence.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.volkswagen-group.com/en/press-releases/powerco-and-quantumscape-announce-landmark-agreement-to-industrialize-solid-state-batteries-18494
- https://www.solidpowerbattery.com/investor-relations/investor-news/news-details/2024/Solid-Power-and-SK-On-Deepen-Partnership-with-New-Agreements/default.aspx
- https://www.solidpowerbattery.com/investor-relations/investor-news/news-details/2026/Solid-Power-Reports-First-Quarter-2026-Results/default.aspx
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 27
MARKET & ECOSYSTEM
Pilot lines are multiplying, but milestones are not directly comparable
The strongest signals combine physical assets, repeatable samples, external validation and a named integration program.
Sources:
Official company announcements | SCULTRA evidence grading
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
27
Program
Physical asset
Cell evidence
Integration evidence
Grade
Honda
27,400 m2 demo line
Prototype program
Internal vehicle path
B
QuantumScape
Cobra equipment
B1 samples
Ducati / PowerCo
A
Solid Power
Pilot + electrolyte
Automotive cells
BMW i7
A
Samsung SDI
S-Line
Vendor-reported 900 Wh/L
OEM pipeline
B
ProLogium
Pilot + Dunkirk plan
Platform samples
Partnered
B
A = external / vehicle evidence | B = asset or vendor evidence
INSIGHT
Compare programs by evidence grade and test conditions, not by the word pilot.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://global.honda/en/newsroom/news/2024/c241121eng.html
- https://ir.quantumscape.com/node/6616/pdf
- https://news.samsungsdi.com/global/articleView?seq=397
- https://ir.solidpowerbattery.com/investor-relations/investor-news/news-details/2025/BMW-Group-and-Solid-Power-are-Testing-All-Solid-State-Battery-Cells-in-a-BMW-I7/default.aspx
- https://prologium.com/manufacturing/expansion-roadmap/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 28
MARKET & ECOSYSTEM
Qualification and traceability will shape the path from cell to vehicle
Safety, durability, pack integrity, carbon-footprint and battery-passport evidence must mature with the chemistry.
Sources:
EU Battery Regulation | UNECE | ISO 6469-1
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
28
1
CELL
Abuse, life, fast charge, temperature, pressure
Repeatability across lots
2
MODULE
Propagation, enclosure, compression, sensing
Failure containment
3
VEHICLE
Crash, environment, charging, controls
System safety and durability
4
MARKET
Carbon footprint, passport, traceability
Regulatory evidence
Standards anchor
UNECE vehicle safety | ISO 6469-1 rechargeable energy storage system requirements | EU Battery Regulation traceability and sustainability
INSIGHT
Qualification evidence should be designed with the cell, because pressure and interface conditions propagate into the module and vehicle.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX%3A32023R1542
- https://unece.org/ev-hev-and-fc
- https://www.iso.org/standard/68665.html
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 29
03
Patent Landscape
How public-family activity reveals crowded terrain, control points and research hypotheses.
SCULTRA REPORT SERIES
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
29
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 30
PATENT LANDSCAPE
The patent view combines a broad WIPO baseline with a focused control-point review
Statistics show momentum; selected families show how claims are forming around materials, interfaces and manufacturing.
Sources:
WIPO | Google Patents | SCULTRA methodology
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
30
LENS 1 | WIPO BASELINE
Published family trend
Purpose
Establish momentum, geography and technical examples using WIPO's solid-state battery annex.
Boundary
Published patent families are not equivalent to active, granted or commercially relevant rights.
LENS 2 | CONTROL POINTS
1
Screen
Public families linked to electrolyte, separator, anode-free and manufacturing themes
2
Code
Map claims to functional control points rather than broad keywords
3
Compare
Test ownership, family scope, filing sequence and product evidence
4
Escalate
Use counsel and official registers for legal-status and FTO work
Illustrative public-family review, accessed August 2026. Technical IP intelligence, not legal opinion or FTO.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 31
PATENT LANDSCAPE
Published solid-state battery families increased sevenfold from 2010 to 2023
The strongest acceleration began after 2017, but recent filing years remain incomplete because of publication lag.
Sources:
WIPO Technology Trends technical annex
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
31
Published solid-state battery patent families
0
500
1000
1500
2000
290
2010
2,033
2023
7.0x
READING THE SIGNAL
Momentum
Activity accelerated strongly after 2017.
Caveat
Recent filing years are incomplete because applications publish with a lag.
Implication
Use families to prioritize claim review, not to rank commercial readiness.
WIPO published-family count. Recent years incomplete because of publication lag.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 32
PATENT LANDSCAPE
Japan owns the deepest historical family base while research output is broadening
Japan accounts for almost 40% of families published from 2000 to 2023; China leads recent scientific publications.
Sources:
WIPO Technology Trends technical annex
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
32
HISTORICAL FAMILY DEPTH
~40%
Japan's share of published families, 2000 to 2023
Deep portfolios from automakers, cell producers and materials companies create a dense partnering and claim environment.
Scientific publications cited in WIPO annex
China
899
United States
587
Japan
295
India
238
Germany
219
South Korea
176
Publication counts indicate research activity, not granted patent strength.
Geography is a portfolio-navigation signal. Verify priority, ownership and legal status family by family.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 33
PATENT LANDSCAPE
The claim terrain clusters around eight recurring technical control points
A functional taxonomy is more useful than a broad keyword count for identifying overlap and white-space hypotheses.
Sources:
WIPO examples | selected public families | SCULTRA taxonomy
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
33
01
Electrolyte composition
Ionic transport, stability, cost
02
Synthesis & particles
Purity, size, morphology, throughput
03
Membrane formation
Thin films, reinforcement, porosity
04
Electrode composite
Contact, loading, active-material coating
05
Lithium interface
Protection, wetting, deposition uniformity
06
Formation protocol
Current, pressure, temperature, lithium inventory
07
Stack & enclosure
Compression, tabs, sealing, edge control
08
Process & inspection
Inline metrology, defect detection, yield
INSIGHT
Crowding is best understood by claim function and dependency, not by counting documents that mention solid-state.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html
- https://patents.google.com/patent/US12159971
- https://patents.google.com/patent/US9966630B2/en
- https://patents.google.com/patent/CN111162276A/en
- https://patents.google.com/patent/US20250030122A1/en
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 34
PATENT LANDSCAPE
Electrolyte claims are moving from composition toward scalable synthesis and membrane formation
Selected families illustrate sulfide composition, synthesis cost, particle control and free-standing film design.
Sources:
Google Patents public-family pages
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
34
SOLID POWER | US12159971B2
Sulfide solid electrolyte composition
Composition and electrochemical properties illustrate continuing optimization of sulfide chemistry.
SOLID POWER | US20250219134A1
Low-cost synthesis and particle control
Recent public application signals value in scalable synthesis, morphology and production economics.
FACTORIAL | US20250030122A1
Composite electrolyte and cell architecture
Claims connect material design with a practical membrane and cell system.
IDEMITSU | EP3637442A4
Sulfide material manufacturing
Materials specialist positioning extends into repeatable production of the electrolyte.
Strategic shift: own the manufacturable material form, not only the nominal chemistry.
Illustrative family review. Claim scope, ownership and status require verification in official registers.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://patents.google.com/patent/US12159971
- https://patents.google.com/patent/US20250219134A1/en
- https://patents.google.com/patent/US20250030122A1/en
- https://patents.google.com/patent/EP3637442A4/en
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 35
PATENT LANDSCAPE
Separator and lithium-metal families focus on thin ceramics, surface treatment and uniform deposition
The defensible interface includes separator microstructure, bonding, protection and cell-level integration.
Sources:
WIPO | Google Patents public-family pages
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
35
QUANTUMSCAPE | US9966630B2
Thin ceramic separator architecture
A dense separator and lithium-metal system place defensibility in microstructure and electrochemical integration.
QUANTUMSCAPE | EP4309228B1
Stack and cell integration
Family signals extend into multilayer assembly and practical cell architecture.
WIPO EXAMPLE | WO2011142150A1
Toyota sulfide battery architecture
Historical example illustrates the depth of Japanese solid-state system research.
INTERFACE CONTROL
Surface treatment and bonding
Opportunity depends on a specific substrate, interface reaction and manufacturable treatment window.
The separator moat is a coupled system of microstructure, surface, process and stack integration.
Selected examples are not a completeness search and do not establish freedom to operate.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html
- https://patents.google.com/patent/US9966630B2/en
- https://patents.google.com/patent/EP4309228B1/en
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 36
PATENT LANDSCAPE
Anode-free claims connect architecture, formation protocol and artificial interphases
Samsung and specialist families show how lithium inventory and plating control become claimable system design.
Sources:
Samsung SDI | Google Patents public-family pages
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
36
SAMSUNG | CN111162276A/B
Anode-free cell architecture
Public family links current-collector design and solid electrolyte to lithium deposition behavior.
FACTORIAL | US20250030122A1
Lithium-metal composite system
Architecture-level claims illustrate dependency between electrolyte, electrodes and formation.
FORMATION PROTOCOL
Lithium inventory as process IP
Current density, temperature and pressure can determine whether anode-free designs form uniformly.
ARTIFICIAL INTERPHASE
Protect, seed and stabilize
Thin coatings or functional layers may become narrow but valuable application-specific claims.
Anode-free defensibility connects a physical interface to a controlled first-cycle protocol.
Research themes are hypotheses for deeper novelty review, not patentability conclusions.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://news.samsungsdi.com/global/articleView?seq=203
- https://patents.google.com/patent/CN111162276A/en
- https://patents.google.com/patent/US20250030122A1/en
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 37
PATENT LANDSCAPE
Manufacturing claims are expanding into stack assembly, enclosures and process control
The control point is shifting from a material recipe to the repeatable production system around it.
Sources:
Google Patents public-family pages | company manufacturing evidence
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
37
QUANTUMSCAPE | EP4309228B1
Multilayer stack construction
Public family illustrates how cell geometry and assembly can carry independent value.
NISSAN | US20240421434A1
All-solid-state battery structure
Recent public application signals continued OEM work on practical cell and enclosure design.
HONDA DEMO LINE
Roll pressing and process verification
Physical assets provide evidence that densification and production sequence are strategic capabilities.
IN-LINE QUALITY CONTROL
Detect buried defects before formation
A high-value white-space hypothesis spans sensing, process feedback and traceability.
Manufacturing IP increasingly protects the repeatable production system around the material.
Patent examples and company evidence are complementary signals, not proof of product coverage.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://patents.google.com/patent/EP4309228B1/en
- https://patents.google.com/patent/US20240421434A1/en
- https://global.honda/en/newsroom/news/2024/c241121eng.html
- https://www.quantumscape.com/quantumscape-releases-next-generation-solid-state-battery-separator-equipment-cobra/
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 38
PATENT LANDSCAPE
Competitive signals point to four defensible layers beyond the base chemistry
Thin-layer manufacture, interface conditioning, pressure architecture and in-line quality control are becoming strategic terrain.
Sources:
Selected public families | official company evidence | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
38
THIN LAYER
Low defect area at high throughput
Material + equipment + inspection
INTERFACE CONDITIONING
Stable contact and controlled interphase
Treatment + formation + data
PRESSURE ARCHITECTURE
Cell life without excessive pack mass
Mechanics + sensing + controls
QUALITY CONTROL
Detect hidden defects before yield loss
Metrology + feedback + traceability
Defensibility potential
SCULTRA synthesis from selected public families and manufacturing evidence. Validate claim relevance at family level.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://patents.google.com/patent/US20250219134A1/en
- https://patents.google.com/patent/EP4309228B1/en
- https://patents.google.com/patent/US20240421434A1/en
- https://global.honda/en/newsroom/news/2024/c241121eng.html
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 39
PATENT LANDSCAPE
White spaces remain where manufacturability, accountability and local capability intersect
These are research hypotheses for deeper novelty and freedom-to-operate work, not patentability conclusions.
Sources:
WIPO | India government sources | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
39
1
Adaptive pressure
Sense swelling and redistribute force through life
PACK MECHANICS + CONTROLS
2
Interface health
Non-destructive signature of contact loss and dendrite risk
SENSORS + ANALYTICS
3
Dry process composite
Low-solvent electrode and electrolyte integration
MATERIALS + EQUIPMENT
4
Formation recipes
Application-specific current, temperature and pressure
PROCESS + DATA
5
Circularity by design
Recovery pathways for sulfide, lithium and current collectors
CELL + RECYCLING
6
India-specific platform
Local precursors, validation, mineral strategy and equipment
ECOSYSTEM + IP
India signal: PLI ACC scale target, National Critical Mineral Mission, patent ambition and IISc interface research create a platform for focused capability building.
White spaces are research hypotheses. Conduct novelty, ownership and FTO analysis before investment or filing.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html
- https://heavyindustries.gov.in/en/pli-acc
- https://www.pib.gov.in/PressNoteDetails.aspx?ModuleId=3&NoteId=155158
- https://dst.gov.in/dst-iisc-energy-storage-platform-moves-towards-enabling-fast-charging-solid-state-batteries
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 40
04
Strategy & Sourcing
How to choose partners, protect differentiation and convert uncertainty into a disciplined program.
SCULTRA REPORT SERIES
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
40
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 41
STRATEGY & SOURCING
Build the layer that encodes application advantage and partner for scale-intensive assets
Control interface know-how, validation data and system design while using partners for chemistry breadth and industrial capacity.
Sources:
SCULTRA strategy synthesis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
41
BUILD
Own differentiated control
Application interface
Formation and operating window
System integration
Validation data and models
PARTNER
Co-develop scarce capability
Electrolyte and membrane
Pilot process transfer
Equipment and metrology
Vehicle or application validation
BUY
Source scale-intensive inputs
Qualified precursors
Standard equipment
Contract testing
Non-differentiating components
OWN THE LEARNING LOOP
Requirements -> cell evidence -> failure analysis -> interface or process change -> system validation -> claim and sourcing update
INSIGHT
Control the knowledge that compounds with every test; avoid owning capital that does not create differentiation.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 42
STRATEGY & SOURCING
Supplier diligence must test evidence quality, not presentation quality
A weighted scorecard should verify cell conditions, repeatability, manufacturability, IP position, supply chain and integration readiness.
Sources:
Official company sources | standards | SCULTRA framework
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
42
Diligence dimension
Weight
Evidence required
Red flag
Cell performance
20%
Format, loading, pressure, temperature, cycle protocol
Single best cell
Repeatability
15%
Lot spread, sample count, third-party or OEM test
No distribution
Manufacturability
20%
Layer thickness, area, throughput, yield, control plan
Lab-only process
IP position
15%
Family map, ownership, licenses, encumbrances
Headline patent count
Supply chain
10%
Precursor purity, capacity, logistics, dual-source plan
Unqualified source
Integration
10%
Module pressure, BMS, thermal, test-vehicle evidence
Cell-only claim
Economics & plan
10%
Capex, conversion cost, ramp assumptions, milestones
Date without gates
Recommended scoring: 1 = unsupported | 3 = credible internal evidence | 5 = repeatable external or production evidence
INSIGHT
Make the supplier reproduce its claim under your intended cell and system conditions.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.volkswagen-group.com/en/press-releases/powerco-confirms-results-quantumscapes-solid-state-cell-passes-first-endurance-test-18031
- https://global.honda/en/newsroom/news/2024/c241121eng.html
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX%3A32023R1542
- https://unece.org/ev-hev-and-fc
- https://www.iso.org/standard/68665.html
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 43
STRATEGY & SOURCING
A 90-day sprint can convert a broad landscape into partner and IP decisions
Sequence market framing, claim mapping, technical validation and sourcing strategy with explicit evidence gates.
Sources:
SCULTRA delivery framework
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
43
DAYS 1-15
Frame
Application economics
Technical boundary
Decision criteria
Opportunity brief
DAYS 16-35
Map
Company longlist
Patent taxonomy
Supply dependencies
Landscape + claim map
DAYS 36-60
Verify
Supplier data room
Expert diligence
Sample test design
Evidence-grade shortlist
DAYS 61-75
Design
Build-buy-partner
IP workplan
Commercial structure
Engagement model
DAYS 76-90
Decide
Partner selection
Pilot charter
Risk and governance
Investment memo
EVIDENCE GATES
Market wedge confirmed | comparable cell data obtained | claim dependencies understood | pilot economics bounded | decision rights assigned
INSIGHT
The 90-day objective is a governed experiment and partner decision, not a final chemistry winner.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- SCULTRA analysis. No external source used.
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]

## Slide 44
CLOSING
The report is a decision framework, not a product ranking or legal opinion
Use the evidence to focus technical diligence, patent work and partnership choices, then refresh milestones before investment decisions.
Sources:
Primary sources accessed 7 August 2026 | SCULTRA analysis
SCULTRA SERVICES
SOLID-STATE BATTERIES & NEXT-GENERATION ENERGY STORAGE
44
HOW TO USE THIS REPORT
1
Focus
Select the application and system constraint worth solving.
2
Verify
Normalize cell evidence and manufacturing conditions.
3
Map
Connect technical control points to public families and partners.
4
Act
Launch a gated pilot with IP, sourcing and evidence workstreams.
SCULTRA SERVICES
From landscape to decision
Technology scouting
Patent landscaping
Supplier assessment
Sourcing strategy
Pilot and negotiation support
Evidence boundary
Primary sources accessed 7 August 2026. Company performance is identified as vendor-reported where applicable. Patent review is illustrative public-family analysis and not legal advice, patentability opinion or FTO. Refresh milestones before investment decisions.
Notes: Prepared as an illustrative SCULTRA report. Validate time-sensitive claims before external publication.
[Sources]
- https://www.wipo.int/web-publications/wipo-technology-trends-technical-annex-the-future-of-transportation-on-land/en/emerging-technology-in-detail-solid-state-batteries.html
- https://www.iea.org/reports/global-ev-outlook-2026/electric-vehicle-batteries
- https://www.nature.com/articles/s41560-023-01208-9
- https://global.toyota/en/newsroom/corporate/39865919.html
- https://www.volkswagen-group.com/en/press-releases/powerco-confirms-results-quantumscapes-solid-state-cell-passes-first-endurance-test-18031
- https://global.honda/en/newsroom/news/2024/c241121eng.html
- https://news.samsungsdi.com/global/articleView?seq=397
- https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX%3A32023R1542
- https://www.pib.gov.in/PressNoteDetails.aspx?ModuleId=3&NoteId=155158
[/Sources]
[QC2 Validation] Reviewed 14 August 2026. Observed facts are source-backed. Third-party forecasts remain estimates. SCULTRA scenarios, scores and recommendations remain analytical judgment. [/QC2 Validation]